## Slide 1
FULL DUPLEX
The Next Inflection Point
in AI Interaction
How vLLM-Omni Enables Models to
Listen and Speak Simultaneously
vLLM-Omni / Real-time conversations
OCTOBER 2026
Notes: The Next Inflection Point in AI Interaction
How vLLM-Omni Enables Models to Listen and Speak Simultaneously
全双工让模型在说话时仍能持续接收用户输入。本次分享介绍 vLLM-Omni 的交互方式、统一运行时架构与性能表现。具体能力随模型和执行模式而异。

## Slide 2
全双工
社区共建
全双工，与社区共同构建
致谢 60+ 贡献者 · 160+ 相关 PR 已合入
vLLM-Omni / 实时音视频会话
2026 年 10 月
01 / 12
代表性已合入 PR
截至 2026 年 10 月 7 日
Native duplex 运行时 · #3907
Unified duplex 框架 · #7413
OpenAI Realtime API · #7285
Qwen3-Omni 接入 · #7585
PersonaPlex unified duplex · #7695
Nemotron VoiceChat · #6089
AURA 接入 · #7633
有界输出传输 · #7644
0xtoward
0z5a
AbelSara
akshatvishu
amy-why-3459
andyluo7
anurag12-webster
BeatSeat
BruceLoveDecimal
CarrotSwordsman
chickeyton
congw729
dshah1333
eval-dev
FayeSpica
frank-2077
Fyrgo8
Gaohan123
GKangaroo
guanzheh
herotai214
Hiro208
hsliuustc0106
HyperbolicCr
IneshReddy249
LHXuuu
linyueqian
LinzeShi
lishunyang12
LOGO127
m0g3r
MrDongsls
natureofnature
NickCao
NolenLiang
NumberWan
psv666
pujitha24
R2-Y
RyanYun09
sphinxkkkbc
StormMelody
stringl1l1l1l
Sy0307
tc-mb
TheCodeWrangler
THUqliu
Tiagosf00
tlysanhuo
twu3202
vraiti
vuuihc
wuli666
xsmccc
xuhuan51
y-null
yenuo26
yuekaizhang
ZacheryAU
ZhengWG
Zhou248
zyforsure
Notes: 全双工能力来自社区持续协作。此页以截至 2026 年 10 月 7 日的社区贡献统计与代表性已合入 PR，展示模型接入、统一框架、Realtime API 和输出传输的共同演进。头像对应社区贡献者，PR 卡片保留可点击链接。
补充技术说明与参考（英文原文）
Full duplex is built with the vLLM-Omni community. This edition recognizes 62 GitHub-linked human contributors across 166 related pull requests merged to main through 7 October 2026. The slide uses rounded lower bounds of 60+ contributors and 160+ PRs.
The portraits credit PR authors and GitHub-linked coauthors on merged commits, in alphabetical order with equal visual weight. Scope includes duplex runtimes, associated model integration and execution, Realtime control, and direct benchmark / validation tooling. Review-only contributions are not included in this count; unlinked signatures are recorded separately without assigning an identity or portrait. Original public GitHub profile avatars link to their respective profiles.
Selected milestones connect native duplex, the unified framework, Realtime interoperability, model integrations and bounded output delivery. The complete attribution is in the companion Community Credits document.
Sources:
- https://github.com/vllm-project/vllm-omni/pull/3907
- https://github.com/vllm-project/vllm-omni/pull/7413
- https://github.com/vllm-project/vllm-omni/pull/7285
- https://github.com/vllm-project/vllm-omni/pull/7585
- https://github.com/vllm-project/vllm-omni/pull/7695
- https://github.com/vllm-project/vllm-omni/pull/6089
- https://github.com/vllm-project/vllm-omni/pull/7633
- https://github.com/vllm-project/vllm-omni/pull/7644

## Slide 3
全双工
体验与交互方式
vLLM-Omni / 实时音视频会话
2026 年 10 月
02 / 12
让音视频会话
持续进行
同一段实时会话
摄像头画面
用户语音
助手语音
barge-in
01
输入输出并行
助手回应时，仍持续接收
用户语音与画面。
02
流式响应
文本与音频增量输出，
无需等待完整回答。
03
实时交互调整
结合新输入，继续回应、调整后续内容或让出话语权。
硬打断：强制停止
客户端 / 服务端控制
显式 cancel 或配置的 VAD 策略
软打断：自主让出话语权 · 依赖模型能力
模型结合持续输入与上下文，
自主决定何时停止发言。
Notes: 全双工体验包括输入输出并行、流式响应，以及结合持续输入调整交互。硬打断由客户端或服务端控制逻辑触发；软打断由具备相应能力的模型结合持续输入与上下文决定何时让出话语权。这里描述体验与能力边界，不表示每个模型都具备相同的自主决策能力。
补充技术说明与参考（英文原文）
Full duplex keeps input and output active within the same session. Responses stream incrementally, while new input can affect what happens next. How that input affects generation depends on the model. MiniCPM's native policy can choose LISTEN or SPEAK; a turn-based model instead starts a new model request from committed input. The timeline is illustrative, not a latency benchmark.
Hard interruption is explicit application/server control, including configured VAD policy. Soft interruption here means model-driven yielding; semantic endpointing alone does not create native LISTEN/SPEAK capability. The client must stop and clear local playback when the protocol signals an interruption.
Sources:
- capabilities.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/capabilities.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py

## Slide 4
全双工
体验与交互方式
不同模型如何处理实时交互
以 Web demo 为例：模型决策、Server VAD 与客户端操作共同决定交互行为。
vLLM-Omni / 实时音视频会话
2026 年 10 月
03 / 12
模型
交互方式
交互效果
MiniCPM-o 4.5
持续接收语音与视频输入
模型决定 LISTEN / SPEAK
在持续会话中聆听或回应
默认不依赖 Server VAD
Qwen3-Omni
Server VAD 检测用户语音
持续接收麦克风输入
清空待播音频
打断当前 response*
AURA
按住说话，松开后
提交新的音视频输入
按住时停止本地播放
服务端仍可继续生成
应用可接入显式 response.cancel，取消服务端当前 response。
模型让出话语权
模型切换到聆听状态
LISTEN 不等于 response.cancel
本地停播
停止用户听到的声音
服务端仍可继续生成
服务端取消
取消当前 response
客户端清空待播音频
* Server VAD 打断需启用 interrupt_response；具体行为取决于模型与所选 demo profile。
Notes: 此页以 MiniCPM、Qwen3-Omni 与 AURA 的 Web demo 为例，区分模型让出话语权、本地停播和服务端取消三种行为。
MiniCPM 持续接收音视频输入，默认由模型自主决定 LISTEN / SPEAK，不依赖 Server VAD。LISTEN 是模型交互决策，不等于显式 cancel。
Qwen3-Omni 的 Server VAD profile 持续接收麦克风输入，收到 speech_started 时停止待播音频，并通过 interrupt_response 启用服务端打断。独立的手动 Realtime profile 使用 duplex=0，回答期间暂停上传，按 input_audio_buffer.commit + response.create 发起生成；它与表中 VAD profile 是不同路径。
AURA 按住说话时停止本地播放，服务端仍可继续生成，松开后 commit 新输入。上述 demo profile 不直接发送 response.cancel；应用可通过公共协议自行接入。取消生成与清理已到达客户端的待播音频是两项不同职责。
参考：
- qwen3_turn.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
- aura_ptt.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py

## Slide 5
全双工
体验与交互方式
接口、会话交互与模型执行方式
vLLM-Omni / 实时音视频会话
2026 年 10 月
04 / 12
接口承载会话交互；执行方式决定模型如何处理输入。
接口
会话交互方式
模型执行方式
典型模型
Chat Completions
/v1/chat/completions
Realtime Duplex
/v1/duplex 或 /v1/realtime?duplex=1
Request–response
Duplex session
每次请求对应一次响应
可选择流式输出
Native duplex execution
持续推理过程中
连续接收输入、输出回应
Turn-based execution
每个已 commit 的 turn
启动一次新的生成请求
Qwen3-Omni
MiniCPM-o 4.5
（turn 模式）
MiniCPM-o 4.5
PersonaPlex
Nemotron VoiceChat
Qwen3-Omni + Server VAD
AURA
Realtime 另有独立的 turn-based 路径：/v1/realtime?duplex=0。
基于 OpenAI Realtime 消息协议，扩展全双工能力
视频输入 · 播放反馈 · 会话续接
Notes: Duplex 消息协议沿用 OpenAI Realtime 的事件体系与消息结构，并扩展视频输入、播放反馈和会话续接能力。/v1/duplex 是 /v1/realtime?duplex=1 的别名，两者使用相同 handler 与消息协议。这里说明协议来源及扩展方向，不表示每个模型都支持全部协议能力，也不承诺所有语义完全等价。
参考：https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/docs/serving/realtime_duplex_api.md#compatibility-with-the-openai-realtime-protocol
区分三个层次：接口、会话交互方式和模型执行方式。Chat Completions 承载 Request–response；Realtime Duplex 承载持续的 Duplex session。在同一个 Duplex session 中，Qwen3-Omni + Server VAD 与 AURA 按 turn 执行，MiniCPM-o 4.5、PersonaPlex 和 Nemotron VoiceChat 采用 native duplex execution。Realtime 还保留独立的 turn-based 路径 /v1/realtime?duplex=0；不能仅凭 Realtime 接口名称判断底层执行方式。
补充技术说明与参考（英文原文）
Distinguish three layers: the interface, the conversation interaction, and the model execution inside a session. Chat Completions carries request–response interactions, optionally streamed. Qwen3-Omni and MiniCPM-o 4.5 in turn mode are representative examples; the list is not exhaustive.
Realtime Duplex opens an engine-owned Duplex session. Use /v1/duplex, or select the Duplex backend explicitly with /v1/realtime?duplex=1. Native duplex execution consumes ongoing input while producing output: MiniCPM-o 4.5, PersonaPlex and Nemotron VoiceChat follow this model-specific path. Turn-based execution buffers a turn and submits a new generation request when it is committed: Qwen3-Omni with Server VAD and AURA are examples. Qwen also supports explicit commit. AURA controls its turns through its model/session policy. The interface remains a streaming session for both execution modes.
Execution mode does not imply identical capabilities. Video input, cancellation, yielding, resume and concurrency vary by model. In particular, MiniCPM LISTEN/SPEAK decisions must not be generalized to every native duplex model. The same model can appear on multiple serving paths when configured accordingly.
/v1/realtime?duplex=0 uses a separate generic turn-based Realtime connection with connection-owned history and a new generation request per committed turn. It does not allocate a Unified Duplex engine session. The unqualified /v1/realtime route selects the backend according to server configuration. The explicit interface labels on this slide avoid equating every WebSocket Realtime connection with Unified Duplex.
Sources:
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/api_server.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/openai.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/realtime/connection.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/capabilities.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js

## Slide 6
全双工
架构与执行流程
Duplex WebSocket 与 Python 会话共用引擎侧会话控制、模型插件和有界输出传输。
vLLM-Omni / 实时音视频会话
2026 年 10 月
05 / 12
统一全双工架构，通信、会话控制与模型计算按层分工
应用 / API 进程
API / Python 事件循环
API Server
协议收发 · attach
event replay
Python
EngineClient
handle · session API
event stream
Duplex Orchestrator
Session
Manager
1. 创建 / 关闭 / 恢复会话，管理 lease
2. 检查容量与积压，分发 command
3. 限制会话输出，清理过期会话
Session
Runner
1. 每个 session 一个，按序消费 mailbox
2. 处理 input / commit / cancel / Stage output
3. 推进 response，更新 history / playback
Model
Plugin
1. 声明能力，准备运行与采样参数
2. 提供会话缓冲，构造 chunk / turn 输入
3. 解释模型输出，适配后续 Stage 策略
command
operation result
session buffer
同一进程 · 独立事件循环
API Server：协议、连接绑定与 event replay
EngineClient：handle、event stream 与控制操作结果
Duplex Orchestrator：会话执行与 Stage 调度
Stage 请求
Stage output
Stage 执行进程
Scheduler + Worker · 计算、KV 与流式缓存
open / close / resume
成功、失败与错误原因
Notes: API Server 处理协议、连接绑定与 event replay；EngineClient 提供 session handle、event stream 和控制操作结果。Duplex Orchestrator 驱动会话执行与 Stage 调度：Session Manager 管理准入、lease、路由和输出限制；Session Runner 按 mailbox 顺序处理输入、commit、cancel 和 Stage output；Model Plugin 提供模型特有的能力、输入构造与输出解释。API 和 Orchestrator 位于同一进程，运行在不同事件循环；Stage 计算由独立进程执行。
补充技术说明与参考（英文原文）
This diagram covers the engine-owned Unified Duplex path. API and Orchestrator run in the same process, on separate event loops/threads; Stage engines and workers run in separate processes. The generic turn-based Realtime handler has a different connection-owned control path.
API Server handles wire events, attachments, replay and event acknowledgements. EngineClient owns typed session handles and event iteration, passes each handle's bounded output buffer to the engine, and routes lifecycle results and exceptional notifications. Manager admits sessions, owns runner/request mappings, checks input and output limits, routes commands and reaps expired sessions. Each Runner consumes its ordered mailbox and coordinates input, response, playback and model work. Plugin supplies capabilities, model state, input construction, output interpretation and stage policies.
Open/close/resume/touch controls and ordinary commands share request_queue, but controls wait for a correlated result while commands return after enqueue. Ordinary text/audio events go directly to the registered per-session DuplexOutputBuffer shared with handle._outbox. Lifecycle results, close notifications and errors without a live output buffer use the global output queue. GPU KV and streaming compute caches belong to Stage workers.
Sources:
- duplex_omni.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
- duplex_omni_engine.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex_omni_engine.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py

## Slide 7
全双工
架构与执行流程
全双工 workflow
API Server 处理协议；EngineClient 提供 session handle；Runner / Plugin 驱动执行。
vLLM-Omni / 实时音视频会话
2026 年 10 月
06 / 12
API / Python 事件循环
独立 Orchestrator 线程
Worker 进程
User Client
采集 · playback
API Server
WebSocket ↔ command / event
EngineClient
session handle · output buffer
Duplex Orchestrator
Session Manager · Runner · Plugin
Stage workers
模型计算 · KV / cache
建立会话：EngineClient 创建 handle + buffer → Manager 完成准入并共用该 buffer → 返回结果
音频 / 视频
command
提交到 Runner mailbox
Plugin 执行计划 → Stage 请求
下一块输入持续到达 · 与 Stage 计算 / 输出交叠
Stage output
每会话 output buffer
handle.events() → API pump
文本 / 音频
playback
playback ACK
command
ACK → 更新播放进度
持续输入 · 每个会话的输出有界 · 独立上报播放进度
Session event ACK 在 API 层处理；playback ACK 进入 Runner，history 更新依模型能力而定。
Notes: 建立会话时，EngineClient 创建 handle 和输出 buffer，Manager 完成准入并共用该 buffer。输入 command 进入 Runner mailbox，由 Plugin 形成 Stage 请求。普通输出经 Manager.emit 直接进入有界的 per-session buffer，再由 handle.events() 和 API pump 发往客户端。新输入可与已有计算和输出交叠。Session event ACK 留在 API 层，playback ACK 进入 Runner；播放进度和 history 的更新规则由模型决定。
补充技术说明与参考（英文原文）
At open, EngineClient creates a handle and its output buffer; Manager admits the session and registers the same buffer object. API input is translated into commands, enqueued through DuplexOmniEngine and dispatched to the Runner mailbox. The Runner and Plugin prepare Stage requests while new input can continue to arrive.
Normal output follows Stage result → Runner/Plugin → Manager.emit → per-session buffer → handle.events() → API event pump → WebSocket. It does not pass through the global output queue first. Buffer limits are 2 MiB and 512 pending ordinary events per session by default. Output overflow fails and closes the affected session; it does not merely pause generation.
Session event ACKs update API-side replay state without entering the Runner. Playback ACKs are commands and update engine playback state according to model rules. Enqueue success is not execution completion: an engine-dead or queue-full error can be returned immediately by the API, while later command rejection is a session event.
Sources:
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- duplex_omni.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- stage_config.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/config/stage_config.py
Workflow 中的交互控制：引擎取消会推进 response epoch，使排队和暂存的旧音频失效，并 abort 关联的 Stage 请求。API 在提交输出传输时再次检查音频有效性。已经到达客户端的音频仍需客户端清理待播队列。模型 LISTEN 决策与这条强制取消路径分开处理。
- qwen3_turn.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
- aura_ptt.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py

## Slide 8
全双工
架构与执行流程
状态处理：持续计算状态与会话历史
MiniCPM 持续更新活跃请求；AURA 与 Qwen3-Omni 按 turn 提交新请求。
vLLM-Omni / 实时音视频会话
2026 年 10 月
07 / 12
模型
输入处理方式
跨 chunk / turn 保留什么
MiniCPM-o 4.5
追加 chunk，继续当前请求
LLM KV / 音频状态；可配置 sliding window
AURA
提交 turn，启动新请求
ASR 文本 / 视频片段 / 助手文本；每轮重建 prompt
Qwen3-Omni
提交 turn，启动新请求
用户音频 / 图像帧 / 对话文本；每轮重建 prompt
MiniCPM-o 4.5
native duplex
持续音视频输入
Multimodal LLM
LLM KV + 流式音频状态
Talker
请求内 TTS 状态
Code2Wav
Decoder cache
SPEAK
LISTEN 保留活跃请求；后续输入复用已绑定的 Replica 和保留的 KV。
AURA
turn-based · 音视频 commit
ASR
音频 → 文本
Thinker
文本 + 视频 + history
Talker
逐句语音 Token
Code2Wav
音频分块
Qwen3-Omni 同属 turn-based：Thinker → Talker → Code2Wav，无独立 ASR Stage。
Stage = 一个模型计算环节；Replica = 同一 Stage 的执行实例。
MiniCPM 的 KV / 流式状态续用以对应请求存活为前提；AURA 的 TTS 可在同一 turn 内续算。
Notes: MiniCPM 对活跃请求持续追加 chunk，复用绑定 Replica 上的 KV 和流式音频状态；LISTEN 保留该活跃请求。AURA 与 Qwen3-Omni 每轮 commit 后提交新的生成请求，并按各自规则重建 prompt。AURA 保留 ASR 文本、视频片段与助手文本；Qwen3-Omni 保留用户音频、图像帧和文本。Stage 指一个模型计算环节，Replica 指同一 Stage 的执行实例；这些计算资源与会话 history 是不同的状态层次。
补充技术说明与参考（英文原文）
MiniCPM appends input to a live resumable Stage-0 request on its bound replica. It retains model KV and streaming audio state. With basic sliding-window mode enabled, its block-aligned path bounds retained context and adjusts positions using in-place Re-RoPE, rather than copying the retained KV window. The retained window is not an unlimited memory of the whole conversation. Talker/Code2Wav state follows the speech request and decoder execution.
AURA commits each turn and rebuilds its Thinker prompt from retained ASR text, video clips and assistant text. Its ASR → Thinker → Talker → Code2Wav path can continue sentence TTS within a turn; a next Thinker turn can overlap draining speech from the prior turn. Qwen similarly submits a new request for committed input, using retained audio, images and text. It has no separate ASR Stage. A commit and cancelling the current response are distinct operations.
A Stage is a compute step. A replica is an execution instance of that Stage, not a duplicate conversation history. The Session Manager and StagePool preserve request affinity needed by resident model state.
Sources:
- stage0.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/stage0.py
- window_kv.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/window_kv.py
- window_plan.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/window_plan.py
- plugin.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py
- plugin.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
播放与 history 的边界：MiniCPM 的 playback ACK 更新播放记录，但不回滚模型 KV。Qwen3-Omni 需要音频完成及完整 playback ACK，才能确认无对齐输出文本已经完整播放。AURA 在 Thinker 完成时提交文本 history，playback ACK 不截断这段 history。
- qwen3_turn.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
- aura_ptt.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py

## Slide 9
全双工
架构与执行流程
恢复连接，延续同一会话
vLLM-Omni / 实时音视频会话
2026 年 10 月
08 / 12
凭会话凭据重新绑定仍存活的 engine session，从上次接收位置续传保留的 event。
User Client
携带会话凭据
从已接收的 event position 发起恢复
API Server
验证凭据并绑定新连接
event replay 补齐保留事件
Engine session
继续使用原有 session state
输入与输出接回同一会话
依赖同一存活 owner、有效 lease 和保留的 event；session resume 不提供进程故障切换。
恢复环节
框架行为
User Client 接入
会话身份
沿用同一 session
Python SDK 自动维护；自定义客户端保存
session ID 与 resume token
连接绑定
新连接接管原会话
重新建立 WebSocket，发送 session.resume
事件续传
续传保留的 event
携带最后接收的 event position
接收仍在 replay window 内的事件
支持活跃会话续接：MiniCPM · AURA · Qwen3-Omni · Nemotron；PersonaPlex 断连后需新建会话。
Notes: Session resume 将新连接重新绑定到仍存活的 engine session，并从最后接收的 event position 续传保留事件。Python SDK 自动维护会话凭据，自定义客户端需要保存 session ID、resume token 和接收位置。恢复依赖原 owner 仍存活、lease 有效，以及所需事件仍在 replay window 内，不提供进程故障切换。MiniCPM、AURA、Qwen3-Omni 和 Nemotron 支持活跃会话续接；PersonaPlex 断连后需新建会话。
补充技术说明与参考（英文原文）
Live-session resume is available for MiniCPM-o 4.5, AURA, Qwen3-Omni and Nemotron in their Unified Duplex paths. The client reconnects to the same live owner, sends session.resume as its first message, and supplies session ID, resume token and last received server event sequence. The server validates the lease and replay window, binds the new attachment, rotates credentials and replays retained events.
PersonaPlex currently advertises supports_session_resume=false; disconnect closes that session. Reconnect therefore opens a new one. Generic turn-based Realtime connection history is also a different path and does not use the engine-owned resume protocol.
Resume depends on the API and engine remaining alive, a valid lease and retained replay events. It is not cross-process failover. A slow or absent consumer can exhaust bounded output/replay capacity, so reconnect does not guarantee that a session will remain available indefinitely. The Python duplex client retains credentials and tracks event position for its reconnect policy.
Sources:
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py
- capabilities.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
- capabilities.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/nemotron_voicechat/duplex/capabilities.py
- duplex.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/clients/duplex.py

## Slide 10
全双工
架构与执行流程
减少重复开销，让语音生成持续提速
从接收音视频到生成语音，减少重复调度，让 GPU 更多时间用于计算。
vLLM-Omni / 实时音视频会话
2026 年 10 月
09 / 12
01
让每小段音视频更快开始计算
MiniCPM-o 4.5 的音视频、Qwen3-Omni 的图像计算可复用预先准备的 GPU 执行流程，
减少 CPU 逐项启动任务的开销。
02
把语音合成中的小操作合并执行
MiniCPM-o 4.5 将语音合成中的多个小操作合并，减少 GPU 任务启动次数，
降低每个音频片段的处理开销。
03
多路会话一起算，已生成的音频不重算
PersonaPlex 将不同会话的新音频帧合成一批处理，语音解码只处理新增帧，
避免反复处理已经生成的内容。
MiniCPM-o 4.5，H100，8 并发请求，Seed-TTS 语音生成
测试日期 | 10 月 5 日 | 10 月 6 日 | 10 月 7 日 | 10 月 8 日
平均 Audio RTF | 0.98 | 0.74 | 0.56 | 0.49
Seed-TTS，Chat Completions 接口。Audio RTF = 音频生成耗时 / 输出音频时长。
按请求取平均，越低越好。测试日期：2026 年 10 月 5–8 日。
Notes: 本页用可直接理解的行为介绍最新主仓中的代表性优化：减少每个输入片段的启动开销、合并语音合成小操作，以及跨 session 处理新音频帧。它们是针对具体模型的执行路径，不表示所有模型都支持或默认启用所有优化。
MiniCPM-o 4.5 对符合条件的流式音频与视觉 encoder 使用 CUDA graph；Qwen3-Omni 本页涉及的是图像 encoder，不能扩展成其视频和音频也使用该路径。CUDA graph 主要减少 CPU 调度和启动开销，不代表省略模型运算。路径受输入 shape、attention 配置及部署 profile 限制，并保留 eager fallback。
MiniCPM-o 4.5 的 Code2Wav 在支持的 CUDA 路径、TF32 开启时默认使用 fused CFM/DiT body，以合并小操作、降低任务启动和中间内存处理开销。关闭 TF32、未支持的结构或缓存类型会改变默认选择或触发 fallback。Resident slot pooling 仍是可选项，浮点融合也不保证波形逐位相同。主仓近期另有输出拷贝异步化改动，本页不展开这层实现细节。
PersonaPlex 将符合条件的多 session 单帧实时追加合并处理，首个携带 persona prefill 的追加仍走原路径。异步 Code2Wav 输入只包含新生成的 codec 帧，同步完整输入每个请求只消费一次，避免重复解码旧内容。这不是对所有并发组合的量化性能承诺。
性能表选取给定数据源中最新的连续四次 H100 每日记录：2026 年 10 月 5–8 日，MiniCPM-o 4.5、Seed-TTS、openai-chat-omni、配置并发 8、128 prompts，导出的 config_key 相同。mean_audio_rtf 分别为 0.9844461966498954、0.7430039011861929、0.559707561533549、0.4902875810555307，表格保留两位小数。每次均完成 128 个请求。该趋势体现近期整体运行结果，不将下降归因于某一个 PR，也不能仅凭导出记录断定部署参数或代码提交完全相同。硬件字段仅写 H100，本页不推断卡数。
这些数据来自 Chat Completions 语音生成测试，不是 8 路 native duplex 实时音视频会话。该 chat benchmark 用请求发出至最后一个音频片段到达的时间作为音频生成耗时，以返回音频解码得到时长，再按请求计算 RTF 并取平均。它不直接证明首播延迟、打断体验或各负载下均无播放卡顿。本次仅核对现有记录，没有重新运行 GPU 测试。数据源链接仅放讲解备注。
Sources:
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/streaming_audio_encoder_graph.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/encoder_cuda_graph.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/minicpmo_4_5_code2wav.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/dit_fused.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/qwen3_omni/vision_encoder_cudagraph.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/worker/gpu_generation_model_runner.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/benchmarks/patch/patch.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/docs/design/minicpm_o45_mrv2_performance.md
- https://github.com/vllm-project/vllm-omni/pull/8430
- https://github.com/vllm-project/vllm-omni/pull/8215
- https://github.com/vllm-project/vllm-omni/pull/8557
- https://github.com/vllm-project/vllm-omni/pull/8356
- https://github.com/vllm-project/vllm-omni/pull/7480
- https://github.com/vllm-project/vllm-omni/pull/8540
- https://hsliuustc0106.github.io/vllm-omni-kanban/pages/assets/charts/minicpmo_4_5_history.json

## Slide 11
全双工
测评与性能
从首包速度到持续交互质量
OmniInteract 与 Omni-DuplexEval 结合实时会话执行，评估响应时序与交互质量。
vLLM-Omni / 实时音视频会话
2026 年 10 月
10 / 12
时间关系示意
计时起点
首个音频包到达
TTFP
请求 / 输出
排队
Stage 计算
传输
音频增量生成与传输
客户端播放
首播
播放与后续生成交叠
响应速度
TTFP · p50 / p95
区分排队、计算与传输
持续输出
RTF · chunk 间隔
停顿与 playback buffer
长会话与并发
持续时长 · session 数
峰值显存 · 资源回收
语音质量
有效音频 · 内容完整性
WER / CER · 听感
统一模型、硬件、并发和计时起点；各模型支持的 benchmark 与测评任务有所不同。
Notes: 实时交互测评需要同时关注响应速度、持续输出、会话时长与并发、语音质量。TTFP 之外，还要观察 RTF、chunk 间隔、播放 buffer、峰值内存与资源回收，以及 WER / CER 和听感。OmniInteract 与 Omni-DuplexEval 已提供执行和测评路径；模型与任务支持范围仍有差异。图中的时间线为关系示意，不是新的实测结果。
补充技术说明与参考（英文原文）
TTFP measures the first received audio packet from a declared timing origin. It differs from audible playback, which includes client buffering and device scheduling. RTF is generation time divided by generated audio duration, so lower is better; audio duration per second is the inverse rate and should be labeled separately. Measure latency distributions, inter-chunk gaps, memory, session duration and speech quality together.
OmniInteract supplies audio/video session execution and timing/evaluation artifacts. Omni-DuplexEval supplies task-oriented native-duplex generation, timing metrics and judging, with a MiniCPM-focused runner and CI guard. Availability of benchmark code does not imply every integrated model supports every task or interaction. Keep hardware, concurrency, input timing and scoring settings fixed when comparing results.
Sources:
- omniinteract.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/omniinteract.py
- omniinteract_eval.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/omniinteract_eval.py
- omni_duplex_eval_runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/duplex/omni_duplex_eval_runner.py
- omni_duplex_eval_metrics.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/duplex/omni_duplex_eval_metrics.py
- README.md: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/tests/e2e/accuracy/omni_duplex_eval/README.md

## Slide 12
全双工
工具调用
全双工模型的工具调用
扩展模型覆盖，统一工具执行期间的交互行为。
vLLM-Omni / 实时音视频会话
2026 年 10 月
11 / 12
当前已支持
Qwen3-Omni Realtime
turn-based Realtime 路径已接入 tool parser
Nemotron VoiceChat
native duplex 支持工具结果回填与续生成
Unified duplex 演进方向
模型输出
工具名称 + 参数
应用执行
外部函数
结果回填
匹配 call_id
模型续生成
生成后续回复
执行期间 | 明确工具执行期间是否继续接收用户输入、输出语音。
轮次隔离 | 处理打断、超时、重复及迟到结果， 避免旧调用影响新一轮交互。
框架与插件分工 | 框架负责公共调用逻辑；插件适配模型输出格式与行为。 扩展至 Qwen3-Omni unified duplex、AURA 与 JoyAI。
Notes: 当前 Qwen3-Omni 的 turn-based Realtime 路径已有 tool parser，Nemotron VoiceChat 的 native duplex 支持工具结果回填与续生成。统一 duplex 的演进范围包括工具名称和参数输出、应用执行、按 call_id 回填结果、模型继续生成，并明确工具执行时输入和语音是否继续。框架负责公共调用与状态规则，插件负责模型格式和行为适配；打断、超时、重复及迟到结果需要与当前 turn 隔离。
补充技术说明与参考（英文原文）
Tool calling already exists in selected vLLM-Omni Realtime serving paths. This slide separates those integrations from the work to provide consistent tool behavior and broader model coverage in the unified duplex framework.
CURRENT SUPPORT
Qwen3-Omni can use the turn-based Realtime handler's tool-parser integration. The handler requires --enable-auto-tool-choice and --tool-call-parser when function tools are active, emits function-call names and argument events, includes function-call results in conversation history, and can generate a subsequent response from that history. This is a separate path from the Qwen3-Omni unified-duplex plugin, which currently raises “Qwen duplex tool calls are not implemented” when realtime_tools is configured. Do not infer that a successful Qwen Realtime tool integration demonstrates support in its unified-duplex deployment.
Nemotron VoiceChat already implements a native-duplex tool-result round trip through the unified framework. It emits function calls, accepts conversation.item.create containing function_call_output with a matching call_id, and queues the tokenized result into its function channel so that the model can continue in the live session. External tools run in the application. The current plugin accepts up to five tools and fixes tools/instructions once the system prompt is resident in model state.
UNIFIED DUPLEX ROADMAP
The common loop covers function names and arguments, application execution, correlated result return, and model continuation. Existing common function-call projection and a plugin hook provide a base. Extending this path requires complete model adapters and consistent behavior across supported models; the framework does not start from zero.
During execution: define independently whether the session continues receiving user input and whether it produces speech while an external tool runs. These are model/policy choices and must not be advertised as a universal behavior. For example, the turn-based Realtime handler suppresses further audio after it observes a tool call; this does not establish a common duplex policy for every model.
Turn safety: associate an outstanding call with its originating session/turn/response generation, define invalidation when a user interrupts or the turn is superseded, handle timeouts, suppress duplicate completion, and prevent late results from entering a newer turn. Common realtime projection already checks a matching completed call_id and rejects duplicate outputs. Those checks should be extended and applied consistently with interruption and timeout rules; this roadmap is not a claim that duplicate protection is entirely missing today. A historical matching call_id alone is not a complete specification of whether a result is still valid for the active turn.
Ownership: the framework should own shared call tracking, result validation, timeout/interruption processing, and stale-result handling. Model plugins should handle model-specific output formats, result encoding and continuation/listen/speak behavior. AURA, JoyAI and the Qwen3-Omni unified-duplex path are adaptation targets, not an assertion that their tool loops are already complete. Application code owns execution of the external function and reports its outcome.
Implementation references (snapshot d5a3380103df2fc827f095c60dbfb6e1c5655fd3):
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L386-L425
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L870-L940
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L1655-L1678
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py#L160-L169
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py#L108-L147
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py#L430-L501
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/realtime_events.py#L1080-L1126
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/realtime_events.py#L1430-L1487
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/plugin.py#L513-L523
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/session/control.py#L290-L327
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/tests/e2e/online_serving/nemotron_voicechat_realtime_duplex.py#L245-L273

## Slide 13
全双工
演进方向
全双工 roadmap
近期完善模型接入、交互能力与测评；远期扩展会话时长和服务规模。
vLLM-Omni / 实时音视频会话
2026 年 10 月
12 / 12
近期
远期
JoyAI 接入
将 JoyAI 接入 unified duplex 框架
完成模型输入与输出适配
通用工具调用
统一调用与结果处理，完善模型适配
处理打断、超时与过期结果
Semantic VAD
结合语义与上下文判断用户是否说完
接入 commit 与 response 策略
扩展实时交互测评
扩展 OmniInteract / Omni-DuplexEval 覆盖
增加模型、交互任务与回归检查
更长且稳定的连续会话
管理长时间音视频会话的 context 与 history
随会话延长，保持稳定的延迟与内存占用
扩大多副本服务规模
通过多个 Stage replica 提升会话并发
支持跨 API frontend 的会话路由与归属管理
Notes: 近期方向：将 JoyAI 接入 unified duplex 框架；完善通用工具调用与模型适配；增加 Semantic VAD；扩展 OmniInteract 和 Omni-DuplexEval 的模型、交互任务和回归覆盖。远期方向：管理更长音视频会话中的 context 与 history，保持延迟和内存稳定；扩大多副本服务规模，完善跨 API frontend 的会话路由与归属管理。当前已有测评路径、MiniCPM sliding window 及 StagePool replica 选择与 affinity，因此后两项强调持续能力和规模扩展。
补充技术说明与参考（英文原文）
Near-term priorities center on model integration, richer interaction and broader evaluation. Longer-term priorities center on sustained conversation duration and serving scale. These priorities build on existing model integrations, evaluation runners and Stage replica infrastructure.
NEAR TERM
JoyAI integration: bring JoyAI into the unified duplex framework through model-specific input/output adapters and shared session orchestration. JoyAI already has model and pipeline code, along with an experimental full-duplex serving path; this priority is integration with the shared runtime rather than first-time model support. Integration does not imply that every model supports native LISTEN/SPEAK or every optional framework capability.
Unified tool calling: standardize function-name/argument output, application-executed functions, correlated result return and model continuation through the shared duplex runtime. Complete model adapters and consistent input/speech behavior, interruption, timeout, duplicate and stale-result handling. The framework already projects function calls and checks matching call IDs and duplicate results; Nemotron VoiceChat supplies a native-duplex function-result hook. The turn-based Realtime handler has tool-parser integration used by Qwen3-Omni, while the Qwen3-Omni unified-duplex plugin explicitly rejects realtime_tools. The priority is shared behavior and broader model coverage, including AURA and JoyAI adapters. The preceding tool-calling slide provides the detailed scope.
Semantic VAD: add meaning-aware turn-completion decisions to the session's commit and response policy. The current validator accepts server_vad only, the acoustic backend uses Silero, and a regression test explicitly rejects semantic_vad. Semantic endpointing is distinct from interruption-intent recognition and from native models' LISTEN/SPEAK decisions. Its inference should stay off the control loop and return ordered, session-scoped decisions, as described in the VAD appendix.
Broader realtime evaluation: extend model, interaction-task, duration, concurrency and regression coverage in OmniInteract and Omni-DuplexEval. Both evaluation paths are already present. Omni-DuplexEval includes generation, scoring and a MiniCPM-focused nightly CI guard. This priority expands and standardizes coverage; it does not introduce evaluation for the first time. Near-term coverage can also establish baselines for the longer-term duration and scaling work.
LONGER TERM
Longer sustained conversations: extend the duration and model coverage of real-time audio/video sessions while managing context, history, memory and latency. MiniCPM-o 4.5 already has model-specific paged-KV/sliding-window infrastructure. The roadmap concerns sustained behavior across growing conversations and more model paths, not an assertion of unlimited context or universal long-session guarantees.
Scaled multi-replica serving: raise concurrent-session capacity across Stage replicas and nodes, then extend session routing and ownership across API frontends. StagePool already chooses available replicas, binds requests and honors affinity; DuplexOrchestrator submits initial and update requests through it. Current duplex endpoints reject multiple API workers because session credentials and replay state remain local to the owning frontend. The concrete remaining direction is scalable session-aware routing, ownership and reliable cleanup while preserving model state affinity. Replica selection alone does not imply that a live model session can migrate its KV state to a different worker.
Implementation references (latest fetched mainline d5a3380103df2fc827f095c60dbfb6e1c5655fd3):
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py#L160-L169
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py#L444-L501
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L386-L425
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/realtime_events.py#L1430-L1487
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/turn_detection.py#L82-L99
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/vad.py#L100-L108
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/tests/engine/duplex/test_engine_session.py#L598-L608
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/benchmarks/omniinteract.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/benchmarks/omniinteract_eval.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/benchmarks/duplex/omni_duplex_eval_runner.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/tests/e2e/accuracy/omni_duplex_eval/README.md
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/minicpmo_4_5/duplex/window_kv.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/stage_pool.py#L574-L609
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex_orchestrator.py#L393-L424
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/api_server.py#L1880-L1895
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/joyai_vl_interaction/pipeline.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/experimental/fullduplex/joyvl/serving/server.py

## Slide 14
全双工
附录 · 架构
全双工执行链路：从输入到模型，再到输出
普通输出通过每个 session 的有界 buffer 传递，由 API 与 Orchestrator 线程共用。
vLLM-Omni / 实时音视频会话
2026 年 10 月
A1
同一 API 进程
API 事件循环
Duplex Orchestrator 线程
User Client · WebSocket
输入 / 请求提交
输出 / 事件回传
API Server
↓ EngineClient · DuplexOmni
↓ DuplexOmniEngine
协议 → handle → command / control
EngineClient → API Server
handle.events() → WebSocket
Session Manager → Runner
mailbox 按序处理 · 会话状态
Model Plugin / ModelChannel
↓ StagePool → Stage client
StagePool → Runner / Plugin
Manager.emit → 共用的 session buffer
request_queue
Janus · 请求
session buffer
有界 · 直接传递
MiniCPM-o 4.5 示例
Thinker
Talker
Code2Wav
Orchestrator / llm2tts
共享内存 connector
StagePool：选择 Replica · 保持 request affinity
同一 Stage 的 Replica · 独立进程
Replica 0 · EngineCore
Scheduler → GPU Worker
Replica 1 · EngineCore
Scheduler → GPU Worker
EngineCoreOutputs
Replica 可位于本机或远端节点
ZMQ
ZMQ
Notes: 这一页展开端到端执行链路。API 事件循环与 Duplex Orchestrator 线程处于同一 API 进程，通过 request_queue 传入 command 和控制操作。普通输出直接进入双方共用的有界 session buffer，API 通过 handle.events() 消费。StagePool 选择可用 Replica，并维持请求 affinity；Replica 内由 EngineCore、Scheduler 和 GPU Worker 完成计算。Replica 可部署于本机或远端；图中 Thinker、Talker、Code2Wav 使用 MiniCPM-o 4.5 举例。
补充技术说明与参考（英文原文）
Read clockwise: API translates a wire event, EngineClient submits it through DuplexOmniEngine, and request_queue delivers commands or lifecycle controls to the Orchestrator. Manager selects the Runner. Plugin and ModelChannel prepare input; StagePool chooses the bound replica and submits to its EngineCore. Scheduler and workers execute the model and return Stage output.
For normal text/audio output, Manager writes directly into the registered per-session buffer. The same object is handle._outbox. handle.events() consumes it and the API pumps events to the WebSocket. The global output queue is a separate path for lifecycle results, close/expiry notifications and errors with no live registered buffer; ordinary audio does not accumulate there.
Session event ACKs are handled at the API attachment layer. Playback ACKs enter the command path. Queue-full and engine-dead errors can return immediately; later rejection arrives as an event. The MiniCPM pipeline at the bottom separates model stages from the process/replica diagram above. Network connectors are required when stages are placed on different nodes.
Session state ownership: SessionManager manages session-to-runner and request-to-session mappings, admission, leases, output bounds and cleanup. Each SessionRunner serializes operations through its mailbox and drives model submission. DuplexEngineSession holds the engine-side turn, response, epoch/fence, request-resource, history and playback state and implements the corresponding update rules. The model plugin creates model-specific session state and supplies buffering, input construction, output interpretation and downstream Stage policy. Worker processes own model KV and streaming caches.
Sources:
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- duplex_omni.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- duplex_omni_engine.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex_omni_engine.py
Session-state implementation references:
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- engine_session.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/engine_session.py
- plugin.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/plugin.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py

## Slide 15
全双工
附录 · 会话控制
Acoustic VAD 与 Semantic VAD
常见组合：Acoustic VAD 先检测停顿，再由 turn detection 模型判断用户是否说完。
vLLM-Omni / 实时音视频会话
2026 年 10 月
A2
对比维度 | Acoustic VAD | Semantic VAD 规划扩展
判断依据 | 语音活动 + 配置的静音时长 | 语义与上下文 音频模型还可结合语调等线索
停顿处理 | 静音达到阈值时可能 commit 即使句子尚未说完 | 判断话语尚未完整时 可继续等待
系统动作 | 静音达到阈值后 commit 输入 按配置自动开始 response | 判断用户说完后 commit 输入 按配置自动开始 response
计算与部署 | CPU 推理开销低 当前：CPU thread pool | 单次判断通常需要更多计算 规划：较重模型在 Omni Stage 执行
开源组合示例：SILERO VAD + PIPECAT SMART TURN v3.2
“帮我订明天的……［停顿］……去北京的机票。”
1. Silero：区分语音 / 非语音，检测停顿
2. Smart Turn：判断话轮完整 / 尚未完整
VAD 可减少非语音噪声造成的误触发。音频降噪与打断意图识别是独立能力。
Session Runner 负责 commit 与打断。检测异步执行，过期结果不再生效。
Notes: Acoustic VAD 判断当前是否存在语音；endpointing 策略再依据静音持续时间决定何时结束话轮。VAD 模型本身不执行 commit，也不直接启动模型生成。
本页的 Semantic VAD 泛指基于语义的 end-of-turn detection。它判断用户当前话语是否完整，可以使用文本上下文，也可以直接从音频中结合语调、节奏等线索判断。
开源例子 Pipecat Smart Turn v3.2 直接接收音频并预测 complete / incomplete。官方推荐与 Silero 等轻量 VAD 配合：VAD 发现停顿后，再把当前话轮累积的音频交给 Smart Turn 判断，无需单独转写。订机票的例子用来说明句中停顿，并非该模型的实测输出。这里展示的是可借鉴的模型组合，不表示它已经接入 vLLM-Omni。
LiveKit 的官方方案同样在 VAD 上叠加 turn detector；其当前音频模型需要 VAD，并结合语义和韵律线索。因此，声学活动检测和语义话轮判断可以作为不同组件组合使用。
API 配置可以要求选择一种模式。例如 OpenAI Realtime 的 turn_detection.type 选择 server_vad 或 semantic_vad。这是 API 策略选择，不能据此推断供应商内部的声学与语义检测组件互斥。
判定话轮结束后，session 才提交输入，并按配置启动 response。判断尚未完整时可继续等待，同时保留系统规定的超时策略。用户开始讲话、是否有意打断助手，以及 native duplex 模型自身的 LISTEN / SPEAK 决策，都不是同一个问题。
本套 vLLM-Omni PPT 中，Semantic VAD 仍为规划扩展。核对的统一 runtime 配置仅接受 server_vad。
References:
- https://github.com/pipecat-ai/smart-turn
- https://huggingface.co/pipecat-ai/smart-turn-v3.2
- https://docs.livekit.io/agents/logic/turns/turn-detector/
- https://developers.openai.com/api/docs/guides/realtime-vad
vLLM-Omni implementation:
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/turn_detection.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/vad.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
计算与部署：轻量 Acoustic VAD 的逐帧推理开销低。Silero 官方参考说明中，30 ms 以上的音频 chunk 可在单 CPU 线程上以不到 1 ms 的时间完成处理。该数值是模型推理时间，不是话轮结束延迟；输入缓冲、排队和配置的静音等待也会影响 commit 时刻。这不是 vLLM-Omni 的实测数据。
Semantic turn detection 通常每次分析更多上下文，但开销取决于模型、硬件和调用频率。Smart Turn 提供 CPU 实现，其项目给出的推理时间为部分 CPU 约 10 ms、多数云实例低于 100 ms。这与 Silero 使用的输入和环境不同，不能直接计算同负载加速比。先用 VAD 检测停顿，再调用语义模型，可以降低语义判断的调用频率。
vLLM-Omni 的规划方向是通过 Omni Stage 执行较重的语义模型，同时保留轻量模型的异步 CPU 执行路径。Omni Stage 是规划设计，不能表述为已经实现的 Semantic VAD 接入，也不保证总延迟一定更低。调度、数据传输、排队和 batching 都需要纳入交互延迟预算。Session Runner 仍负责决定继续等待、commit 或启动 response。
噪声处理：VAD 判断语音活动，可以减少非语音噪声导致的语音事件误触发；它不会输出降噪后的波形，不会去掉混在人声中的噪声，也不能可靠排除背景中的其他人声。音频降噪、回声消除和目标说话人过滤是独立处理能力。示例也不表示 native duplex 路径应该丢弃所有非语音音频 chunk。
Additional references:
- https://github.com/snakers4/silero-vad
- https://github.com/pipecat-ai/smart-turn
Runtime placement and session policy:
当前 VAD 属于 unified duplex 会话运行时：Session Runner / Manager 管理每个 session 的检测状态和策略，共享 Silero ONNX backend，检测通过 CPU 线程池异步执行，与 Orchestrator 同处 API 进程，但不阻塞控制循环。Semantic VAD 可复用这一职责划分：轻量方案使用独立 CPU pool，较大模型采用独立加速器 worker 或服务。判断结果带上 session、输入序号和 epoch，回到 Runner 按序应用并丢弃过期结果。
补充技术说明与参考（英文原文）
For the Unified Duplex path, Server VAD belongs to the Orchestrator session runtime. SessionManager supplies the process-shared Silero ONNX backend; each session keeps independent detector state. Runner offloads CPU detection to a thread pool and applies the resulting speech-onset, endpointing, commit and interruption policy on its control loop. These CPU threads remain in the API/Orchestrator process. MiniCPM native duplex does not require Server VAD by default. The generic turn-based Realtime connection is a separate control path.
Semantic VAD is a proposed extension here, not an integrated feature. A lightweight model can run in a bounded CPU pool, preferably reusing streaming ASR. A larger model can use a separate accelerator service with bounded batching latency. Decisions should carry session/input sequence/epoch so the Runner can apply them in order and discard stale work. Turn completion and model-native yielding are different decisions.
Sources:
- vad.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/vad.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- connection.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/realtime/connection.py
Semantic VAD 的规划执行位置：轻量模型使用异步 CPU pool。Smart Turn 这类原生音频模型无需 ASR，基于文本的 endpointing 模型可以复用流式转写。较重模型通过 Omni Stage 执行，并限制队列长度和 microbatch 等待时间。这里是规划扩展：Stage 返回话轮完成度判断，Session Runner 负责等待、commit、response 策略，并验证 session、输入序号与 epoch 后应用结果。需要计算传输和排队成本，不能直接假定放到加速器上总延迟就更低。
Additional references:
- https://github.com/snakers4/silero-vad
- https://github.com/pipecat-ai/smart-turn

## Slide 16
全双工
附录 · 会话控制
断连、cancel 与 close，各自影响什么
MiniCPM、AURA、Qwen3-Omni 与 Nemotron 支持活跃会话续接；PersonaPlex 断连即关闭会话。
vLLM-Omni / 实时音视频会话
2026 年 10 月
A3
触发操作
正在执行的工作
会话与恢复
断连 · 支持续接的模型
可继续生成；记录后续事件
断连 grace 内、会话仍存活时可续接
response.cancel
取消当前 response，使其待发音频失效
会话保留；已取消回复不恢复
session.close / lease 过期
终止并清理关联请求
会话结束；重新交互需新建
会话仍存活
在断连 grace 内恢复
session 仍由存活的 owner 持有
会话凭据有效
resume token 有效
lease generation 匹配
保留事件可续传
提供最后接收的 event position
所需 event 仍在保留范围内
默认：断连 grace 30s · idle TTL 300s · replay 60s / 8 MiB。恢复依赖同一仍存活的 owner。
Notes: 断连、response.cancel 和 session.close 各有不同效果。对支持续接的模型，断连后会话可在 grace 内继续存活，后续输出进入事件记录；response.cancel 终止当前 response 并使其待发音频失效，会话仍保留；close 或 lease 过期则清理会话与关联工作。恢复要求 owner 仍存活、凭据有效、lease generation 匹配，且所需 event 仍可续传。默认 disconnect grace 为 30 秒，idle TTL 为 300 秒，replay 为 60 秒 / 8 MiB。
补充技术说明与参考（英文原文）
Disconnect, response cancellation and session termination affect different state. For a resumable model, a dropped connection can leave the engine session and in-flight generation alive during the disconnect grace. response.cancel cancels the response, invalidates old queued audio and preserves the session. session.close or lease expiry terminates the session and releases its associated work.
Resume depends on session lifetime, valid credentials and replay coverage. The same live owner must still hold the session; the disconnect grace and lease must permit reattachment. The server validates the resume token and lease generation. The client's last received event position must be covered by retained events. Resume reattaches to existing state; cancelled work remains cancelled and a closed or expired session cannot be resurrected. Main slide 08 presents the client-facing reconnection flow.
MiniCPM-o 4.5, AURA, Qwen3-Omni and Nemotron support live-session resume. PersonaPlex closes its session on disconnect. Current defaults are a 30-second disconnect grace, 300-second idle TTL, and a replay window bounded by 60 seconds and 8 MiB. These are configuration defaults, not guarantees of process failover or persistent recovery.
Sources:
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py
- stage_config.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/config/stage_config.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py

## Slide 17
全双工
附录 · 部署
跨机 Stage 共用入口侧的 Orchestrator
单个 API worker 持有 duplex session；Head 连接本机及已注册的 headless Stage 进程。
vLLM-Omni / 实时音视频会话
2026 年 10 月
A4
Head 节点
API / EngineClient / Duplex Orchestrator
本机 Stage 0 · EngineCore / Worker
节点 B · headless
Stage 1 · EngineCore / Worker
节点 C · headless
Stage 2 · EngineCore / Worker
请求 / 输出
1 统一部署配置
统一模型拓扑；session_mode: duplex
配置设备与网络 connector
2 启动 Head
stage-id 0 启动单个 API worker 与本机 Stage
提供可访问的 master 地址与端口
3 部署侧启动 headless
指定 stage-id 与同一 master
向 OmniMaster 注册，启动本机 Stage
Headless Stage 共用 Head Orchestrator；duplex 不支持多 API worker，跨机传输需配置网络 connector。
Notes: 跨节点部署时，入口 Head 持有 API、EngineClient 和 Duplex Orchestrator，本机或远端 headless Stage 向 OmniMaster 注册，由同一入口侧 Orchestrator 调度。部署侧使用同一拓扑配置，指定 session_mode: duplex、设备与网络 connector；先启动 Head，再启动指定 stage-id 的 headless 进程。当前 duplex 不支持多个 API worker；多个 Stage 或 Replica 不意味着每个 Stage 各自持有一个 Duplex Orchestrator。
补充技术说明与参考（英文原文）
The Head process owns the API/EngineClient and its Duplex Orchestrator. It starts the selected local stage and discovers other stage/replica processes through OmniMaster registration. Each headless process starts its assigned Stage engines/workers; it does not create a separate Duplex Orchestrator for that stage.
Use a consistent deploy topology, reachable master address/port and network-capable connectors for cross-node Stage data. SharedMemory connectors are local-host transports. The Head Orchestrator dispatches to StagePool clients and preserves request affinity.
Current duplex endpoints reject configurations with multiple API workers, since attachment credentials and replay state are owner-local. Scaling stage replicas is different from scaling API workers, and a distributed Stage layout does not supply transparent frontend failover. The diagram illustrates deployment ownership; model/device/connector support must match the chosen configuration.
Sources:
- api_server.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/api_server.py
- stage_runtime.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/stage_runtime.py
- stage_init_utils.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/stage_init_utils.py

## Slide 18
全双工
附录 · 参考代码
参考代码
vLLM-Omni / 实时音视频会话
2026 年 10 月
A5
层次
实现入口
阅读重点
API 通信适配
OmniDuplexSessionHandler
协议 event、连接绑定与 replay
EngineClient
DuplexOmni / DuplexSessionHandle
handle、共享 output buffer 与 event
通信与传输
DuplexOmniEngine / DuplexOutputBuffer
控制队列与有界 session 输出
会话运行时
DuplexSessionManager / DuplexSessionRunner
lease、状态、mailbox 与模型策略
Stage 编排
DuplexOrchestrator / StagePool
初始请求、后续更新与副本绑定
模型执行
Scheduler / Model Worker
batching、计算与模型缓存
Notes: 参考代码按职责列出阅读入口：API 通信适配、EngineClient、通信与传输、会话运行时、Stage 编排和模型执行。先区分 command、控制操作结果与普通 session 输出，再对应到 Manager / Runner、StagePool、Scheduler 和 Model Worker。图中的类名与方法名保留英文，便于对应源码。
补充技术说明与参考（英文原文）
The references link to one source snapshot. The engine queue carries commands and lifecycle control messages. Ordinary output uses the handle's shared DuplexOutputBuffer; the global output queue remains for control results and exceptional session notifications. Follow Manager/Runner for session ownership, StagePool for replica selection, and Scheduler/Worker for model compute and retained caches.
Sources:
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- duplex_omni.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
- duplex_omni_engine.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex_omni_engine.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py