## Slide 1
The Next Inflection Point
in SI Interaction
How vLLM-Omni Enables Models to
Listen and Speak Simultaneously
Notes: The Next Inflection Point in SI Interaction
How vLLM-Omni Enables Models to Listen and Speak Simultaneously
全双工让模型在说话时仍能持续接收用户输入。本次分享介绍 vLLM-Omni 的交互方式、统一运行时架构与性能表现。具体能力随模型和执行模式而异。

## Slide 2
全双工
社区共建
双工，与社区共同构建
致谢 60+ 贡献者 · 160+ 相关 PR 已合入
vLLM-Omni / 实时音视频会话
2026 年 10 月
01 / 13
代表性已合入 PR
截至 2026 年 10 月 7 日
Native duplex 运行时 · #3907
Unified duplex 框架 · #7413
OpenAI Realtime API · #7285
Qwen3-Omni 接入 · #7585
PersonaPlex unified duplex · #7695
Nemotron VoiceChat · #6089
AURA 接入 · #7633
取消后丢弃待发音频 · #7644
0xtoward
0z5a
AbelSara
akshatvishu
amy-why-3459
andyluo7
anurag12-webster
BeatSeat
BruceLoveDecimal
CarrotSwordsman
chickeyton
congw729
dshah1333
eval-dev
FayeSpica
frank-2077
Fyrgo8
Gaohan123
GKangaroo
guanzheh
herotai214
Hiro208
hsliuustc0106
HyperbolicCr
IneshReddy249
LHXuuu
linyueqian
LinzeShi
lishunyang12
LOGO127
m0g3r
MrDongsls
natureofnature
NickCao
NolenLiang
NumberWan
psv666
pujitha24
R2-Y
RyanYun09
sphinxkkkbc
StormMelody
stringl1l1l1l
Sy0307
tc-mb
TheCodeWrangler
THUqliu
Tiagosf00
tlysanhuo
twu3202
vraiti
vuuihc
wuli666
xsmccc
xuhuan51
y-null
yenuo26
yuekaizhang
ZacheryAU
ZhengWG
Zhou248
zyforsure
Notes: 这里的双工指整个社区建设的服务能力，覆盖 native duplex 模型以及通过 duplex session 服务的 turn-based 模型，并不表示每个模型都具备原生全双工能力。
全双工能力来自社区持续协作。此页以截至 2026 年 10 月 7 日的社区贡献统计与代表性已合入 PR，展示模型接入、统一框架、Realtime API 和输出传输的共同演进。头像对应社区贡献者，PR 卡片保留可点击链接。
补充技术说明与参考（英文原文）
Full duplex is built with the vLLM-Omni community. This edition recognizes 62 GitHub-linked human contributors across 166 related pull requests merged to main through 7 October 2026. The slide uses rounded lower bounds of 60+ contributors and 160+ PRs.
The portraits credit PR authors and GitHub-linked coauthors on merged commits, in alphabetical order with equal visual weight. Scope includes duplex runtimes, associated model integration and execution, Realtime control, and direct benchmark / validation tooling. Review-only contributions are not included in this count; unlinked signatures are recorded separately without assigning an identity or portrait. Original public GitHub profile avatars link to their respective profiles.
Selected milestones connect native duplex, the unified framework, Realtime interoperability, model integrations and bounded output delivery. The complete attribution is in the companion Community Credits document.
Sources:
- https://github.com/vllm-project/vllm-omni/pull/3907
- https://github.com/vllm-project/vllm-omni/pull/7413
- https://github.com/vllm-project/vllm-omni/pull/7285
- https://github.com/vllm-project/vllm-omni/pull/7585
- https://github.com/vllm-project/vllm-omni/pull/7695
- https://github.com/vllm-project/vllm-omni/pull/6089
- https://github.com/vllm-project/vllm-omni/pull/7633
- https://github.com/vllm-project/vllm-omni/pull/7644
PR #7644 bounds each session output buffer and rejects cancelled audio before delivery. The client must still stop audio already received.
Source: https://github.com/vllm-project/vllm-omni/pull/7644

## Slide 3
全双工
概览
目录
vLLM-Omni / 实时音视频会话
2026 年 10 月
02 / 13
核心内容
全双工背景、交互方式与模型
vLLM-Omni 统一架构与流程
性能优化与评测指标
工具调用与演进方向
技术附录
更详细的架构与执行流程
VAD 与打断机制
会话生命周期与恢复
跨机部署
Notes: 正文依次介绍全双工背景、交互方式与模型，vLLM-Omni 统一架构和执行流程，性能优化和评测指标，以及工具调用和演进方向。技术附录进一步展开架构与执行路径、VAD 与打断机制、会话生命周期与恢复、跨机部署；参考代码位于附录末尾。

## Slide 4
全双工
体验与交互方式
vLLM-Omni / 实时音视频会话
2026 年 10 月
03 / 13
从半双工到全双工交互
半双工
轮流发言
摄像头
用户
助手
全双工
边听边说
摄像头
用户
助手
用户插话
→
共有能力：流式响应
两种模式都可增量输出文本与音频。
输入输出并行
助手回应期间，
仍持续接收新输入。
实时交互调整
native duplex 模型结合新输入，
调整后续输出或让出话语权。
Notes: 讲解顺序：先看左侧半双工，再看右侧全双工，最后看下方能力对比。
半双工示例按用户发言、助手回应交替进行。全双工示例展示助手发言时用户继续输入，模型可结合后续输入调整输出或让出话语权。共有能力是文本和音频的流式输出；这不是全双工独有能力。
本页比较交互体验，不把所有 turn-based execution 一概等同于半双工。Qwen3-Omni + VAD 的会话可在播放期间接收输入，后续由 VAD 与 commit 驱动新请求；模型级持续输入与控制机制在 A2 展开。
时间线只是说明先后关系和输入输出重叠，不表示真实延迟或模型性能排名。摄像头轨道代表具备相应视觉输入能力的示例，并非所有模型都支持视频。
Technical detail and source references
This slide compares interaction experiences. Half-duplex means input and output take turns in the illustrated client experience; it is not a label for every turn-based model or transport. The half-duplex camera frames likewise accompany the accepted input segments. Full-duplex allows incoming user speech to overlap assistant output, with camera input continuing in this illustrated multimodal configuration. Waveform spacing is schematic, not a latency benchmark. Camera/video support depends on the model and configuration.
Streamed responses are a shared capability: a turn-based or half-duplex experience can still generate and deliver audio/text incrementally. Native duplex models add the ability to use ongoing input within model execution to influence subsequent output or choose to yield. Qwen3-Omni + Server VAD instead buffers committed turns and supports externally triggered interruption; that distinction is detailed in Appendix A2. The detailed diagram and explicit-cancel versus VAD paths have been relocated there.
Sources:
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/examples/online_serving/realtime_web/app/static/profiles/minicpm_native.js
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/examples/online_serving/realtime_web/app/static/app.js
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/model_executor/models/minicpmo_4_5/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/model_executor/models/minicpmo_4_5/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/engine/duplex/session/model_channel.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/engine/duplex/session/overlap_policy.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/engine/duplex/vad.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/minicpmo_4_5/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/personaplex/README.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/docs/design/fullduplex-personaplex.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/deploy/personaplex.yaml
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/tests/engine/duplex/test_session_runner_personaplex.py

## Slide 5
全双工
体验与交互方式
不同模型如何处理实时交互
交互控制方式取决于模型能力与所选 demo。
vLLM-Omni / 实时音视频会话
2026 年 10 月
04 / 13
模型
输入处理
回复控制
MiniCPM-o 4.5
持续接收语音与视频
模型决定 LISTEN 或 SPEAK
Qwen3-Omni + VAD
持续接收麦克风输入
配合 Server VAD
VAD 触发停止播放
以及服务端取消生成*
AURA demo
按住说话，松开提交
按住时停止本地播放；
服务端仍可能继续生成
PersonaPlex：显式 cancel 会重置对话上下文；断连后需新建 session。
模型自主发言
PersonaPlex · MiniCPM-o 4.5
模型决定何时发言
本地停播
AURA 按钮 · Qwen VAD demo
停止本地播放，推理仍可能继续
服务端取消
Qwen3-Omni + Server VAD*
取消当前生成
* 各模型的 demo 控制方式不同；Qwen VAD 取消需启用 interrupt_response。
PersonaPlex
持续接收流式语音
持续接收语音的同时，
模型生成语音或保持静默
Notes: 本表按“输入处理”和“回复控制”比较。PersonaPlex 与 MiniCPM-o 展示模型自主行为；Qwen3-Omni + Server VAD、AURA demo 展示所选服务端策略与客户端操作，不代表模型固有且唯一的交互方式。PersonaPlex 的音色和角色配置不属于回复控制，因此从表中移除。下方三个机制说明框保持不变。Qwen VAD 取消服务端生成需要启用 interrupt_response。
The bottom cards are examples of mechanisms, not a feature checklist shared by every model. Native models continuously process input during output; AURA can make a per-commit silent/speak decision but does not append new input to one live Thinker request. Local playback stop does not by itself cancel inference.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/plugin.py#L236-L258
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js#L14-L20
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js#L8-L29
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py#L374-L388
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/personaplex/README.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/docs/design/fullduplex-personaplex.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/deploy/personaplex.yaml
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/tests/engine/duplex/test_session_runner_personaplex.py

## Slide 6
全双工
体验与交互方式
接口、会话交互与模型执行方式
vLLM-Omni / 实时音视频会话
2026 年 10 月
05 / 13
接口承载会话交互；执行方式决定模型如何处理输入。
接口
会话交互方式
模型执行方式
典型模型
Chat Completions
/v1/chat/completions
Realtime Duplex
/v1/duplex 或 /v1/realtime?duplex=1
Request–response
Duplex session
每次请求对应一次响应
可选择流式输出
Native duplex execution
持续推理过程中
连续接收输入、输出回应
Turn-based execution
每个已 commit 的 turn
启动一次新的生成请求
Qwen3-Omni
MiniCPM-o 4.5
（turn 模式）
PersonaPlex
MiniCPM-o 4.5
Nemotron VoiceChat
Qwen3-Omni + Server VAD
AURA
Realtime 另有独立的 turn-based 路径：/v1/realtime?duplex=0。
基于 OpenAI Realtime 消息协议，扩展全双工能力
扩展能力按模型提供：视频输入 · playback feedback · session resume
Notes: PersonaPlex demonstration and model-specific behavior
PersonaPlex is a speech-only, native duplex model on the unified /v1/duplex endpoint (also /v1/realtime?duplex=1). It is always clocked in 80 ms audio units: 1920 samples at 24 kHz. This is a codec/model frame duration, not an end-to-end latency guarantee. Input is framed by the session; clients may send different chunk sizes. The model continues hearing the user during its own speech. There are no client commits or external turn signals, and no Server VAD is required to gate generation. The plugin's decide_output returns None: do not label its behavior as MiniCPM's discrete LISTEN/SPEAK decision path.
Voice comes from bundled voice prompts; persona comes from session instructions. Both are fixed for the lifetime of a session. This is not arbitrary voice cloning. The former standalone Moshi-compatible web demo has been removed; the current integration uses the unified endpoint and DuplexClient preset.
Stage 0 is the Talker: worker-side streaming Mimi input encoding, temporal transformer and Depformer. The framework keeps a live resumable Stage 0 request, with KV managed through the model runner; the worker runtime retains per-session encoder state and frame history. Stage 1 is Code2Wav with a separate streaming Mimi decoder per request. Codes cross the shared-memory connector and only new PCM is returned. These are two Stages, not three Stages for the encoder, temporal model and Depformer. State is isolated by request/session and epoch.
Overlapping speech is native model behavior. supports_barge_in=false and supports_audio_truncate=false: do not promise playback-position rewind or destructive barge-in semantics. response.cancel and output_audio_buffer.clear advance the epoch, abort the live request and replay voice/persona prefill on the next fresh request. The engine session may remain open, but its previous model conversation context is discarded. These explicit commands are different from speaking while the model is talking.
supports_session_resume=false: a transport drop closes the PersonaPlex session. A reconnect creates a new session; reusing voice/persona configuration does not restore earlier KV or codec state. The resume diagram applies only to the models named as resumable. The MiniCPM RTF chart on 10/13 remains a MiniCPM benchmark, not a PersonaPlex measurement.
Duplex 消息协议沿用 OpenAI Realtime 的事件体系与消息结构，并扩展视频输入、播放反馈和会话续接能力。/v1/duplex 是 /v1/realtime?duplex=1 的别名，两者使用相同 handler 与消息协议。这里说明协议来源及扩展方向，不表示每个模型都支持全部协议能力，也不承诺所有语义完全等价。
参考：https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/docs/serving/realtime_duplex_api.md#compatibility-with-the-openai-realtime-protocol
区分三个层次：接口、会话交互方式和模型执行方式。Chat Completions 承载 Request–response；Realtime Duplex 承载持续的 Duplex session。在同一个 Duplex session 中，Qwen3-Omni + Server VAD 与 AURA 按 turn 执行，MiniCPM-o 4.5、PersonaPlex 和 Nemotron VoiceChat 采用 native duplex execution。Realtime 还保留独立的 turn-based 路径 /v1/realtime?duplex=0；不能仅凭 Realtime 接口名称判断底层执行方式。
补充技术说明与参考（英文原文）
Distinguish three layers: the interface, the conversation interaction, and the model execution inside a session. Chat Completions carries request–response interactions, optionally streamed. Qwen3-Omni and MiniCPM-o 4.5 in turn mode are representative examples; the list is not exhaustive.
Realtime Duplex opens an engine-owned Duplex session. Use /v1/duplex, or select the Duplex backend explicitly with /v1/realtime?duplex=1. Native duplex execution consumes ongoing input while producing output: MiniCPM-o 4.5, PersonaPlex and Nemotron VoiceChat follow this model-specific path. Turn-based execution buffers a turn and submits a new generation request when it is committed: Qwen3-Omni with Server VAD and AURA are examples. Qwen also supports explicit commit. AURA controls its turns through its model/session policy. The interface remains a streaming session for both execution modes.
Execution mode does not imply identical capabilities. Video input, cancellation, yielding, resume and concurrency vary by model. In particular, MiniCPM LISTEN/SPEAK decisions must not be generalized to every native duplex model. The same model can appear on multiple serving paths when configured accordingly.
/v1/realtime?duplex=0 uses a separate generic turn-based Realtime connection with connection-owned history and a new generation request per committed turn. It does not allocate a Unified Duplex engine session. The unqualified /v1/realtime route selects the backend according to server configuration. The explicit interface labels on this slide avoid equating every WebSocket Realtime connection with Unified Duplex.
Sources:
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/api_server.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/openai.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/realtime/connection.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/capabilities.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
PersonaPlex source references:
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/personaplex/README.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/docs/design/fullduplex-personaplex.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/deploy/personaplex.yaml
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/tests/engine/duplex/test_session_runner_personaplex.py

## Slide 7
全双工
架构与执行流程
Duplex WebSocket 与 Python 会话共用引擎侧会话控制、模型插件和有界输出传输。
vLLM-Omni / 实时音视频会话
2026 年 10 月
06 / 13
统一全双工架构，通信、会话控制与模型计算按层分工
应用 / API 进程
API / Python 事件循环
API Server
协议收发 · attach
event replay
Python
EngineClient
session handle
command / event routing
Duplex Orchestrator
Session
Manager
1. 创建 / 关闭 / 恢复会话，管理 lease
2. 检查容量与积压，分发 command
3. 管理有界 output buffer，清理过期会话
Session
Runner
1. 每个 session 一个，按序消费 mailbox
2. 处理 input / commit / cancel / Stage output
3. 推进 response，更新 history / playback
Model
Plugin
1. 声明能力，准备运行与采样参数
2. 提供会话缓冲，构造 chunk / turn 输入
3. 解释模型输出，适配后续 Stage 策略
command / 会话操作
operation result
session event
同一进程 · 独立事件循环
API Server：协议、连接绑定与 event replay
EngineClient：handle、event stream 与控制操作结果
Duplex Orchestrator：会话执行与 Stage 调度
Stage 请求
Stage output
Stage 执行进程
Scheduler + Worker · 计算、KV 与流式缓存
open / close / resume
成功、失败与错误原因
Notes: Commands and lifecycle operations cross the same engine request transport. Open, close and resume use control-result correlation; ordinary session outputs go directly to the bounded buffer shared with the handle. EngineClient owns handles and routes command/event traffic; the Orchestrator runs session control and Stage dispatch on its own event loop in the same process.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/engine/duplex_omni_engine.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/entrypoints/duplex_omni.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/engine/duplex/session/manager.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex_omni_engine.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py

## Slide 8
全双工
架构与执行流程
全双工 workflow
API Server 处理协议；EngineClient 路由 command 与 event；Orchestrator 协调会话执行。
vLLM-Omni / 实时音视频会话
2026 年 10 月
07 / 13
API / Python 事件循环
独立 Orchestrator 线程
Stage 进程
User Client
采集 · playback
API Server
WebSocket ↔ command / event
EngineClient
session handle · output buffer
Duplex Orchestrator
Session Manager · Runner · Plugin
Stage engines
Scheduler · Worker · KV / cache
建立会话：EngineClient 创建 handle + buffer → Manager 完成准入并共用该 buffer → 返回结果
音频 / 视频
command
提交到 Runner mailbox
构造输入 → 提交 Stage 执行
下一块输入持续到达 · 与 Stage 计算 / 输出交叠
Stage output
每会话 output buffer
handle.events() → API pump
文本 / 音频
playback
playback ACK
command
ACK → 更新播放进度
Native：追加到持续请求 · Turn-based：commit 后启动新请求 · 两种模式均可持续接收输入
Session event ACK 在 API 层处理；playback ACK 进入 Runner，history 更新依模型能力而定。
Notes: The diagram represents framework I/O concurrency. Continued input reception does not mean every model immediately incorporates it into a running generation. Native plugins append to a live request; Qwen3-Omni and AURA wait for committed input to start fresh requests. Stage execution includes EngineCore scheduling and workers. Event acknowledgments terminate at the API; playback acknowledgments go to the session runtime.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/config/stage_config.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py

## Slide 9
全双工
架构与执行流程
vLLM-Omni / 实时音视频会话
2026 年 10 月
08 / 13
从实时输入到语音输出：Stage 与状态
native duplex 续用计算状态；turn-based execution 根据历史构建新请求。
模型 / 输入
Stage → 语音输出
持续保留的内容
PersonaPlex
native duplex
PCM 音频 · 80 ms / 帧
计算状态
S0：KV + Mimi encoder
S1：Mimi decoder
MiniCPM-o 4.5
native duplex
PCM 音频 + 视频
计算状态
S0：LLM KV + 音频状态
LISTEN 保留活跃请求
AURA
turn-based · commit
PCM 音频 + 视频
对话历史
ASR 文本 + 视频片段
+ 助手文本
Qwen3-Omni
turn-based · commit
PCM 音频 + 图像
对话历史
用户音频 + 图像
+ 对话文本
S0 · Talker
Mimi 编码 · Temporal · Depformer
S1 · Code2Wav
Mimi → 24 kHz PCM
8 组 audio codebooks
S0 · LLM
音频 + 视频
S1 · Talker
生成 audio tokens
S2 · Code2Wav
Tokens → PCM
SPEAK：文本 + 特征
Audio tokens
S0 · ASR
音频 → 文本
S1 · Thinker
文本 + 视频
S2 · Talker
文本 → tokens
S3 · Code2Wav
Tokens → PCM
文本
文本
Audio tokens
S0 · Thinker
音频 + 图像
S1 · Talker
生成 audio tokens
S2 · Code2Wav
Tokens → PCM
文本 + 特征
Audio tokens
PCM = 音频波形 · Audio tokens = codec 编码 · KV = 模型 attention cache
Notes: 讲解顺序：每次看一行，依次说明输入、Stage、箭头上的数据，以及右侧保留的状态。S0、S1 等编号属于各模型自己的 pipeline。
PersonaPlex：PCM 音频输入，Stage 0 内部包含 Mimi encoder、Temporal Transformer 和 Depformer；Stage 间传助手侧 8 组 audio codebooks，经时间对齐后送至 Stage 1 的 Mimi decoder，输出 PCM。encoder 不是第三个 Stage，也不在 API Server 或 Orchestrator 中执行。80 ms 是模型音频帧时长，不是端到端延迟。Stage 0 保留 KV 与 encoder state，Stage 1 保留 decoder state。
MiniCPM-o 4.5：S0 多模态 LLM 处理音频与视频；SPEAK 将文本与模型特征送至 Talker，再以 audio tokens 送至 Code2Wav。LISTEN 保留活跃请求。后续 native 输入续用 LLM KV 与流式音频状态，并受配置的窗口策略管理。TTS 与解码状态用于语音生成请求，不能扩大为所有下游状态始终跨整个会话保留。
AURA：ASR → Thinker → Talker → Code2Wav。ASR 输出文本，Thinker 结合文本、视频和历史生成回复文本；语音阶段生成 tokens 并解码为音频。按上下文策略保留 ASR 文本、视频片段和助手文本，每个 commit 启动新生成请求。Thinker 完成后，下一轮可开始，而上一轮语音合成仍可继续。
Qwen3-Omni：Thinker → Talker → Code2Wav，没有单独的 ASR Stage。Thinker 接收用户音频、图像帧和上下文，其文本及模型特征供 Talker 使用。后续 turn 复用用户音频、图像帧和对话文本等历史，在 commit 后构建新请求。
右列区分跨 native 输入续用的计算状态，以及跨 turn 复用的会话历史。turn-based 模型在单个回复内也可保留流式解码状态。Stage 是一个模型计算阶段；Replica 是 Stage 的执行实例；一个 Stage 可以包含多个内部模块。
四种模型都使用 PCM 音频。MiniCPM 官方 Web demo 使用 16 kHz pcm16 输入，Python preset 默认 24 kHz pcm16 输出；PersonaPlex preset 使用 24 kHz pcm_f32le 输入与 24 kHz pcm16 输出。AURA Web 使用 16 kHz pcm16，Qwen3 turn Web 使用 24 kHz PCM，插件侧消费归一化后的 16 kHz pcm_f32le。PCM 格式与 native / turn-based 执行方式属于不同维度。
Technical detail and source references
Presenter flow for 08/13
Read one model row at a time: incoming media, compute stages, transmitted data, then the state carried into the next input. Stage numbers are local to each model pipeline, not a cross-model execution sequence. The pale rows use the same visual treatment for all models. Blue marks native duplex and teal marks turn-based execution.
PersonaPlex: PCM in, audio codec tokens between stages, PCM out. The client preset sends mono 24 kHz pcm_f32le and receives 24 kHz pcm16 via Base64 WebSocket payloads. The session input buffer groups audio into 1920-sample / 80 ms units; 80 ms is a frame duration, not an end-to-end latency. Stage 0 contains streaming Mimi encoding plus Temporal Transformer and Depformer. The inter-stage adapter selects eight assistant codebooks, compensates their acoustic delays and packs them codebook-major. Stage 1 Mimi decoding emits float32 waveform samples; the output adapter performs the requested wire encoding. Stage 0 retains temporal KV and Mimi encoder state; Stage 1 retains Mimi decoder state. The encoder is not a third Stage and does not run in the API Server or Orchestrator.
MiniCPM-o 4.5: stage 0 is the multimodal LLM; SPEAK passes text and model features to the Talker, followed by codec tokens to Code2Wav. LISTEN retains the live request rather than starting speech synthesis. LLM KV and streaming audio state are reused across native input appends, with the configured window policy. Downstream TTS and decoder state belongs to the speech-generation request, not a generic promise to preserve all downstream state for the whole session. The live request remains associated with its selected Stage replica.
AURA: the stages are ASR, Thinker, Talker and Code2Wav. ASR produces text. Thinker uses the transcript, video and conversation context, then supplies text to the speech stages. Context carried into future turns consists of ASR text, retained video clips and assistant text, under the session context policy. A new committed turn creates a new generation request. The next turn can begin after Thinker completes while the prior speech synthesis continues.
Qwen3-Omni: Thinker, Talker and Code2Wav; no separate ASR Stage. The Thinker consumes user audio/image frames plus conversation context; its text/embeddings and hidden features condition Talker. Codec tokens go to Code2Wav. Retained context includes user audio, image frames and conversation text, subject to configured limits. Input can arrive during output, but a committed turn starts fresh generation rather than appending to a continuously running native model request.
Scope: the right column contrasts live computation retained across native inputs with conversation history reused for fresh turn-based requests. It is not an exhaustive list of every transient runtime buffer. Turn-based speech synthesis may retain decoder state within a response. Stage means a model-compute step; a replica is an execution instance of a Stage. A Stage can contain several internal modules.
Source baseline: upstream main b65107d61331327424910c72e7a2da137dcfb3df; the relevant model pipeline/plugin/processor files are unchanged from the previously inspected f3391da7c snapshot. This is a targeted slide rewrite; the rest of the deck retains its previous source baselines.
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/clients/personaplex.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/personaplex/pipeline.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/stage_input_processors/personaplex.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/minicpmo_4_5/pipeline.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/minicpmo_4_5/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/minicpmo_4_5/duplex/policy.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/aura_omni/pipeline.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/qwen3_omni/pipeline.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/model_executor/stage_input_processors/qwen3_omni.py
Earlier source references retained for traceability:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/aura_omni/duplex/history.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/window_kv.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/window_plan.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/personaplex/README.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/docs/design/fullduplex-personaplex.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/deploy/personaplex.yaml
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/tests/engine/duplex/test_session_runner_personaplex.py
Audio terminology clarification
All four model rows accept PCM audio in their unified duplex paths. PCM describes sampled audio; it does not distinguish native duplex from turn-based execution. The MiniCPM-o 4.5 web profile sends pcm16 at 16 kHz; its Python client preset inherits the same input default and pcm16 at 24 kHz output from SessionConfig. PersonaPlex uses its own preset: pcm_f32le at 24 kHz input and pcm16 at 24 kHz output. AURA web input is pcm16 at 16 kHz. The Qwen3 turn web profile uses audio/pcm at 24 kHz, while its plugin consumes normalized 16 kHz pcm_f32le. All these are PCM representations. Codec tokens between stages are a separate representation.
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/examples/online_serving/realtime_web/app/static/profiles/minicpm_native.js
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/clients/duplex.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/vllm_omni/clients/minicpmo_4_5.py
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
https://github.com/vllm-project/vllm-omni/blob/b65107d61331327424910c72e7a2da137dcfb3df/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js

## Slide 10
全双工
架构与执行流程
连接恢复：按模型能力处理
vLLM-Omni / 实时音视频会话
2026 年 10 月
09 / 13
支持 session resume：MiniCPM-o 4.5、AURA、Qwen3-Omni 与 Nemotron VoiceChat。
User Client
携带会话凭据
从已接收的 event position 发起恢复
API Server
验证凭据并绑定新连接
event replay 补齐保留事件
Engine session
继续使用原有 session state
输入与输出接回同一会话
在 session 有效期间，重新连接到同一个仍存活的 API 进程。
事件 replay 依赖保留窗口；进程重启后需新建 session。
恢复环节
框架行为
User Client 接入
会话身份
沿用同一 session
保存 session ID 与最新的 resume token；
Python WebSocket SDK 会管理这两项凭据。
连接绑定
新连接接管原会话
新连接的首条消息发送 session.resume；
保存 session.resumed 返回的新 token。
事件续传
续传保留的 event
提供最后接收的 event sequence。
若所需事件已缺失，则新建 session。
PersonaPlex demo：断连后新建 session，并重新应用原有音色与 persona。
Notes: Resume is a model-dependent serving capability and is separate from automatic reconnect in a particular demo. The Python WebSocket client retains credentials and can reconnect with its configured reconnect policy. A reconnect sends session.resume as its first message, with session ID, resume token and last received server-event sequence. Successful attachment rotates the token and returns it in session.resumed. The client saves the latest token. Replay gaps return session.resync_required and cannot transparently reconstruct missing output. Process restart or loss of the owner requires a fresh session. PersonaPlex does not support resume and closes on disconnect.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/clients/duplex.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/entrypoints/duplex/session_attachment.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/nemotron_voicechat/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/clients/duplex.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/personaplex/README.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/docs/design/fullduplex-personaplex.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/deploy/personaplex.yaml
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/tests/engine/duplex/test_session_runner_personaplex.py

## Slide 11
全双工
测评与性能
性能优化方法与持续改进
减少重复工作，让 GPU 更多时间用于有效计算。
vLLM-Omni / 实时音视频会话
2026 年 10 月
10 / 13
CUDA Graphs：减少重复调度
复用准备好的 GPU 执行流程，降低 CPU 调度开销。
MiniCPM-o 4.5 · Qwen3-Omni（图像）· PersonaPlex
Kernel fusion：合并小操作
减少 GPU 任务启动次数和中间数据搬运。
MiniCPM-o 4.5
Session batching：多路会话一起算
将多个会话的新音频帧合成一批处理。
PersonaPlex
Incremental decoding：只解码新音频
保留解码状态，只处理新增的音频 chunk。
PersonaPlex
H100 · Chat Completions
Chart: MiniCPM-o 4.5
| 9/9 | 9/10 | 9/11 | 9/12 | 9/13 | 9/14 | 9/15 | 9/16 | 9/17 | 9/18 | 9/19 | 9/20 | 9/21 | 9/22 | 9/23 | 9/24 | 9/25 | 9/26 | 9/27 | 9/28 | 9/29 | 9/30 | 10/1 | 10/2 | 10/3 | 10/4 | 10/5 | 10/6 | 10/7 | 10/8
单并发 | 0.27964 | 0.30571 | 0.28627 | 0.29968 | 0.28142 | 0.33544 | 0.29289 | 0.25669 | 0.25745 | 0.26584 | 0.2664 | 0.25163 | 0.26437 | 0.26153 | 0.26986 | 0.24026 | 0.23423 | 0.23092 | 0.23214 | 0.23604 | 0.22503 | 0.23295 | 0.23398 | 0.23219 | 0.21993 | 0.19845 | 0.20049 | 0.19807
8 并发 | 1.5947 | 1.6391 | 1.6005 | 1.5331 | 1.4274 | 1.5488 | 1.4436 | 1.2232 | 1.2144 | 1.2032 | 1.2285 | 1.217 | 1.2343 | 1.2296 | 1.1505 | 1.1635 | 1.1365 | 1.1195 | 0.95724 | 0.97135 | 0.95412 | 0.91499 | 0.95614 | 0.97211 | 0.98445 | 0.743 | 0.55971 | 0.49029
Audio RTF 越低越好
Seed-TTS · 2026 年 9 月 9 日至 10 月 8 日；虚线跨越无同配置测试记录的日期。
Audio RTF = 音频生成耗时 / 输出音频时长，按请求取平均。
Notes: 单并发与 8 并发曲线使用同配置的 H100 Seed-TTS 测试记录，覆盖 2026 年 9 月 9 日至 10 月 8 日。
9 月 16、17 日没有匹配配置的记录。虚线仅连接两侧真实测量点，表示缺测区间；原始数据、真实点数量和嵌入 Excel 中的空单元格都不变。
Audio RTF 是每个请求的音频生成耗时除以输出音频时长，再取平均，越低越好。这是 Chat Completions 语音生成测试，不是连续音视频 native duplex 会话测试。趋势与左侧优化方法并列展示，不把时间变化归因于某一个独立优化。
Technical detail and source references
MiniCPM-o 4.5 benchmark trend for a 30-calendar-day window ending with the latest matching H100 run: September 9 to October 8, 2026. Endpoint and backend: openai-chat-omni. Dataset: Seed-TTS. Concurrency 1: 32 requests per run. Concurrency 8: 128 requests per run. All selected runs completed without failed requests. Each series uses one unchanged config_key. One latest matching record per day; no matching records on September 16 or 17, bridged by dashed visual connectors. The figure contains 28 observed points per series and does not add missing measurements. Dashed connectors join the surrounding measured endpoints as a visual guide only; the chart data and embedded workbook retain empty cells for September 16 and 17. Mean Audio RTF is the mean per-request audio-generation-time / output-audio-duration ratio, lower is better. These are Chat Completions speech-generation benchmarks, not continuous native audio/video session measurements. Changes over time are observational and not an isolated attribution to any one optimization listed on the left.
First and last values: C=1 0.279637232 to 0.198065725; C=8 1.594658489 to 0.490287581.
Source: https://hsliuustc0106.github.io/vllm-omni-kanban/pages/assets/charts/minicpmo_4_5_history.json
Source generated_at: 2026-10-09T02:35:21.650129
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/streaming_audio_encoder_graph.py
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/encoder_cuda_graph.py
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/minicpmo_4_5_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/dit_fused.py
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/qwen3_omni/vision_encoder_cudagraph.py
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/worker/gpu_generation_model_runner.py
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/benchmarks/patch/patch.py
https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/docs/design/minicpm_o45_mrv2_performance.md
https://github.com/vllm-project/vllm-omni/pull/8430
https://github.com/vllm-project/vllm-omni/pull/8215
https://github.com/vllm-project/vllm-omni/pull/8557
https://github.com/vllm-project/vllm-omni/pull/8356
https://github.com/vllm-project/vllm-omni/pull/7480
https://github.com/vllm-project/vllm-omni/pull/8540
https://hsliuustc0106.github.io/vllm-omni-kanban/pages/assets/charts/minicpmo_4_5_history.json

## Slide 12
全双工
测评与性能
从首包速度到持续交互质量
结合 OmniInteract、Omni-DuplexEval 与延迟、流式输出指标，评估实时交互。
vLLM-Omni / 实时音视频会话
2026 年 10 月
11 / 13
时间关系示意
输入流开始
首个音频包到达
Stream TTFP
输入 / 输出
输入 / 排队
Stage 计算
传输
音频增量生成与传输
客户端播放
首播
播放与后续生成交叠
首音频延迟
Stream TTFP · p50 / p95
输入开始 → 收到首个音频包
持续输出
Response RTF · chunk 间隔
停顿与播放缓冲
长会话与并发
持续时长 · session 数
峰值显存 · 资源回收
交互质量
何时回应 · 回应内容
音视频理解
TTFP 衡量首包到达时间；真正何时开始回答，需结合交互测评判断。
比较指标时需统一计时窗口；测评覆盖范围因模型而异。
Notes: The timing illustration now explicitly uses stream TTFP: input-stream start until the client receives its first audio packet. It is not end-of-utterance latency or per-response server TTFP. The current metric collector has separate stream and response origins; comparisons must use the same origin, model, hardware and concurrency. Response RTF and stream RTF are not interchangeable. OmniInteract and Omni-DuplexEval provide model/task-specific interaction evaluation; the quality card emphasizes response timing and audiovisual understanding rather than implying all listed models share a speech-quality score. The figure is a schematic, not a measured timing trace.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/benchmarks/duplex_session_metrics.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/benchmarks/omniinteract.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/benchmarks/duplex/omni_duplex_eval_metrics.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/omniinteract.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/omniinteract_eval.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/duplex/omni_duplex_eval_runner.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/duplex/omni_duplex_eval_metrics.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/tests/e2e/accuracy/omni_duplex_eval/README.md

## Slide 13
全双工
工具调用
全双工模型的工具调用
基于已有工具调用路径，扩展更多模型在统一双工框架中的支持。
vLLM-Omni / 实时音视频会话
2026 年 10 月
12 / 13
当前已支持
Qwen3-Omni Realtime
工具调用解析 · /v1/realtime?duplex=0
Nemotron VoiceChat
统一 native duplex 中的工具调用与结果回填
下一步：扩展统一双工工具调用支持
模型输出
工具名称 + 参数
应用执行
外部函数
结果回填
匹配 call_id
模型续生成
生成后续回复
执行期间 | 明确工具执行期间是否继续接收用户输入、输出语音。
轮次隔离 | 处理打断、超时、重复及迟到结果， 避免旧调用影响新一轮交互。
框架与插件分工 | 框架提供公共处理逻辑，各模型通过 plugin 适配。 扩展 Qwen3-Omni unified duplex、AURA 与 JoyAI 的支持。
Notes: Qwen3-Omni tool-call parsing exists in the separate Realtime turn endpoint (duplex=0). It must not be confused with the Qwen unified duplex + Server VAD adapter. Nemotron VoiceChat already supports tool calls and tool results through unified native duplex. The lower sequence and table describe broader common handling and model coverage to build on these implementations. Work includes interruption, timeout and duplicate/late-result handling, plus explicit input/output behavior while tools execute.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/entrypoints/openai/realtime/session.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L386-L425
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L870-L940
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L1655-L1678
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py#L160-L169
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py#L108-L147
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py#L430-L501
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/realtime_events.py#L1080-L1126
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/realtime_events.py#L1430-L1487
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/plugin.py#L513-L523
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/session/control.py#L290-L327
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/tests/e2e/online_serving/nemotron_voicechat_realtime_duplex.py#L245-L273

## Slide 14
全双工
演进方向
全双工 roadmap
近期完善模型接入、交互能力与测评；远期扩展会话时长和服务规模。
vLLM-Omni / 实时音视频会话
2026 年 10 月
13 / 13
近期
远期
JoyAI 接入
将 JoyAI 接入 unified duplex 框架
完成模型输入与输出适配
通用工具调用
扩展更多模型的工具调用支持
处理打断、超时与迟到结果
Semantic VAD
结合语义与上下文判断用户是否说完
接入 commit 与 response 策略
扩展实时交互测评
扩展 OmniInteract / Omni-DuplexEval 覆盖
增加模型、交互任务与回归检查
更长且稳定的连续会话
管理长时间音视频会话的 context 与 history
随会话延长，保持稳定的延迟与内存占用
扩展到多个 API worker
在现有 Stage replica 支持上继续扩展
增加跨 API frontend 的会话路由与归属管理
Notes: The longer-term scale goal builds on existing StagePool replica routing and request affinity. It is not the first introduction of Stage replicas. The current unified duplex WebSocket path requires one API worker because session credentials and replay state are process-local. Routing/ownership across multiple API frontends is future work. Longer sessions extend existing context/history controls rather than claim that current sessions are necessarily short. JoyAI unified adaptation, broader tool handling, semantic endpointing and broader evaluation are proposed priorities, not release-date commitments.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/entrypoints/openai/api_server.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/engine/duplex_omni_engine.py
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py#L160-L169
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py#L444-L501
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L386-L425
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/realtime_events.py#L1430-L1487
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/turn_detection.py#L82-L99
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/vad.py#L100-L108
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/tests/engine/duplex/test_engine_session.py#L598-L608
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/benchmarks/omniinteract.py
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/benchmarks/omniinteract_eval.py
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/benchmarks/duplex/omni_duplex_eval_runner.py
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/tests/e2e/accuracy/omni_duplex_eval/README.md
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/minicpmo_4_5/duplex/window_kv.py
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/stage_pool.py#L574-L609
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex_orchestrator.py#L393-L424
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/api_server.py#L1880-L1895
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/joyai_vl_interaction/pipeline.py
https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/experimental/fullduplex/joyvl/serving/server.py

## Slide 15
全双工
附录 · 架构
全双工执行链路：从输入到模型，再到输出
普通输出通过每个 session 的有界 buffer 传递，由 API 与 Orchestrator 线程共用。
vLLM-Omni / 实时音视频会话
2026 年 10 月
A1
同一 API 进程
API 事件循环
Duplex Orchestrator 线程
User Client · WebSocket
输入 / 请求提交
输出 / 事件回传
API Server
↓ EngineClient · DuplexOmni
↓ DuplexOmniEngine
协议 → handle → command / control
EngineClient → API Server
handle.events() → WebSocket
Session Manager → Runner
mailbox 按序处理 · 会话状态
Model Plugin / ModelChannel
↓ StagePool → Stage client
StagePool → Runner / Plugin
Manager.emit → 共用的 session buffer
request_queue
Janus · 请求
session buffer
有界 · 直接传递
PersonaPlex 示例
Talker · Stage 0
Mimi Code2Wav · Stage 1
同机 shared-memory 音频编码传输
StagePool：选择 Replica · 保持 request affinity
同一 Stage 的 Replica · 独立进程
Replica 0 · EngineCore
Scheduler → GPU Worker
Replica 1 · EngineCore
Scheduler → GPU Worker
EngineCoreOutputs
Replica 可位于本机或远端节点
ZMQ
ZMQ
Notes: The two PersonaPlex compute stages are Talker (Stage 0) and Mimi Code2Wav (Stage 1). The connector example at the bottom is shared-memory transfer on one host. The upper replica topology can also be distributed, in which case Stage-to-Stage data requires a network-capable connector as shown in A4. Per-session ordinary output remains a bounded shared buffer within the API process.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/deploy/personaplex.yaml
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/engine/duplex/session/manager.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex_omni_engine.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/engine_session.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/personaplex/README.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/docs/design/fullduplex-personaplex.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/deploy/personaplex.yaml
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/tests/engine/duplex/test_session_runner_personaplex.py

## Slide 16
全双工
附录 · 会话控制
vLLM-Omni / 实时音视频会话
2026 年 10 月
A2
模型发言决策
与 VAD 打断
同一段实时会话
01
模型决定何时发言
新输入持续进入模型计算。
模型自主决定继续发言或让出话语权。
02
VAD 驱动的 turn-taking
检测到用户发声时，打断当前回复。
静音达到阈值后 commit，启动新请求。
两种取消入口
LISTEN 是模型决策，与这两条路径不同。
显式 response.cancel
客户端 command 进入会话取消处理。
底层取消逻辑停止当前生成。
VAD 触发打断
用户发声触发 overlap policy。
复用底层取消逻辑；客户端停止播放。
摄像头
用户语音
Barge-in：用户插话
MiniCPM-o 4.5 · native duplex
模型决定 LISTEN / SPEAK；已排队音频可继续播放。
Qwen3-Omni + VAD · turn-based
用户发声停止生成与播放；静音达到阈值后 commit。
VAD 触发打断
VAD commit
模型：LISTEN
VAD commit
Notes: 本页承接体验对比，分别说明 MiniCPM 的模型决策路径和 Qwen3-Omni + VAD 的控制路径。
MiniCPM 接收持续输入，由模型决定 LISTEN / SPEAK。LISTEN 不是 response.cancel，也不会清空客户端已排队的播放音频。时间线表示模型生成状态，已排队音频可能继续播放。
Qwen3-Omni + VAD：首次用户语音结束并达到静音阈值后，VAD 自动 commit 并启动回复。播放期间用户再次发声，服务端按 overlap policy 取消当前生成，客户端停止并清理播放；这一段输入结束后再次 VAD commit，启动新的生成请求。
显式 response.cancel 与 VAD 触发打断是两个入口。前者是客户端发送的 command，后者由服务端语音活动检测触发 overlap policy。二者复用底层取消逻辑，但 VAD 并不是发送了同一个 response.cancel 协议消息；输入缓冲的处理也可能不同。
时间线对齐用于说明事件顺序，不比较实测延迟，不代表所有模型支持相同打断行为。
Technical detail and source references
The figure compares two execution paths using the same illustrative input. The output waveforms represent model-generated audio, not the precise time at which a device plays or stops it. The two output tracks are aligned to avoid suggesting a latency ranking or measured equality. Barge-in labels the user's overlapping speech; it is not the literal barge_in command in either illustrated path.
MiniCPM-o 4.5 native example: the web profile continuously appends audio/video, enables auto_response, sends no commit messages, and does not enable Server VAD. The model chooses LISTEN / SPEAK as new chunks arrive. A model LISTEN is projected through the model-output path; it is not an automatic invocation of the runner's hard-cancel path. The web client's listen event changes model/interaction state without clearing the playback queue, so already queued audio can finish. The illustration shows one model choice to yield; the model may instead keep speaking. Later speech follows native continuation rather than a VAD commit. Explicit framework barge_in/cancel is a separate supported control mechanism for MiniCPM and is not depicted here.
Qwen3-Omni + Server VAD example: the web profile keeps microphone upload enabled during playback, sets overlap_policy=barge_in_on_speech, and enables interrupt_response/create_response. VAD speech onset drives the runner overlap-cancellation path. The client's speech_started handling stops local playback and clears queued audio, including when server generation has already completed. After the configured silence threshold, VAD schedules commit and create_response. The plugin requires a committed turn and starts a fresh model request. This configuration does not wait for Qwen to autonomously decide whether to yield.
Source snapshot: f3391da7c58ee8dc990829aab82166edf865d19b. The relevant runtime, plugin and web-profile files are unchanged from the preceding reviewed snapshot 4c5541cfc17143f80bdb89bbb7a5840b08bb52c6.
Sources:
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/examples/online_serving/realtime_web/app/static/profiles/minicpm_native.js
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/examples/online_serving/realtime_web/app/static/app.js
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/model_executor/models/minicpmo_4_5/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/model_executor/models/minicpmo_4_5/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/engine/duplex/session/model_channel.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/engine/duplex/session/overlap_policy.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/f3391da7c58ee8dc990829aab82166edf865d19b/vllm_omni/engine/duplex/vad.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/minicpmo_4_5/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/personaplex/README.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/docs/design/fullduplex-personaplex.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/deploy/personaplex.yaml
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/tests/engine/duplex/test_session_runner_personaplex.py
VAD commit is shown for both Qwen turns. The first commit follows the initial user utterance and the configured silence threshold; create_response=true then starts the first model request. A later user interruption can cancel the old response, followed by a second VAD commit after that utterance and silence. No cancellation is implied for the initial turn when no assistant response exists. The commit markers are on the Qwen path only. Marker positions express event order, not measured silence durations or response latency. The current Qwen VAD web preset uses silence_duration_ms=500; this is configurable.
VAD-triggered interruption names a behavior, not a protocol command. The runner handles VAD overlap with _barge_in_for_overlap and shares the core _cancel_active_response helper with explicit response.cancel. It does not synthesize a response.cancel wire message. Explicit response.cancel arrives as CancelResponse, is resolved, and enters _on_cancel. These paths also differ in input-buffer handling. Local playback stop is performed by the web client in response to speech-start/interruption events.

## Slide 17
全双工
附录 · 会话控制
Acoustic VAD 与 Semantic VAD
常见组合：Acoustic VAD 检测停顿，再由 turn-end detector 判断用户是否说完。
vLLM-Omni / 实时音视频会话
2026 年 10 月
A3
对比维度 | Acoustic VAD | Semantic VAD 规划扩展
判断依据 | 语音活动 + 配置的静音时长 | 语义与上下文 音频模型还可结合语调等线索
停顿处理 | 静音达到阈值时可能 commit 即使句子尚未说完 | 判断话语尚未完整时 可继续等待
系统动作 | 可在静音后自动 commit。 按配置决定是否生成 response。 | 判断用户说完后 commit 输入 按配置自动开始 response
计算与部署 | CPU 推理开销低 当前：CPU thread pool | 轻量模型可在 CPU 上运行 较重模型：计划接入 Omni Stage
开源组合示例：SILERO VAD + PIPECAT SMART TURN v3.2
“帮我订明天的……［停顿］……去北京的机票。”
1. Silero：区分语音 / 非语音，检测停顿
2. Smart Turn：判断话轮完整 / 尚未完整
VAD 可减少非语音噪声造成的误触发。音频降噪与打断意图识别是独立能力。
Server VAD：Runner 执行 commit / cancel 策略；检测计算在其事件循环之外运行。
Notes: Acoustic VAD identifies speech/non-speech; endpointing also uses a silence policy. Semantic turn-end detection uses learned linguistic/acoustic cues to judge whether the user has finished. The two can be combined: Silero detects a pause and Smart Turn checks completion. Smart Turn v3.2 is a lightweight CPU-capable example; semantic detection does not inherently require a GPU Stage. An Omni Stage for heavier models is a proposed integration, not current implementation. Current Server VAD inference is asynchronous in a CPU executor outside the Orchestrator event loop; the Runner applies configured commit/cancel policy. VAD is not a denoiser, and utterance completion is not interruption-intent detection.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/engine/duplex/vad.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/engine/duplex/session/runner.py
https://github.com/pipecat-ai/smart-turn
https://huggingface.co/pipecat-ai/smart-turn-v3.2
https://docs.livekit.io/agents/logic/turns/turn-detector/
https://developers.openai.com/api/docs/guides/realtime-vad
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/turn_detection.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/vad.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
https://github.com/snakers4/silero-vad
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/realtime/connection.py

## Slide 18
全双工
附录 · 会话控制
断连、cancel 与 close，各自影响什么
MiniCPM、AURA、Qwen3-Omni 与 Nemotron 支持活跃会话续接；PersonaPlex 断连即关闭会话。
vLLM-Omni / 实时音视频会话
2026 年 10 月
A4
触发操作
正在执行的工作
会话与恢复
断连 · 支持续接的模型
可继续生成；记录后续事件
断连 grace 内、会话仍存活时可续接
response.cancel
终止生成，丢弃尚未发出的输出
session 保留；PersonaPlex 重置模型上下文
session.close / lease 过期
终止并清理关联请求
会话结束；重新交互需新建
会话仍存活
在断连 grace 内恢复
session 仍由存活的 owner 持有
会话凭据有效
session ID + 最新 resume token
成功续接后 token 会更新
保留事件可续传
最后接收的 event sequence
所需事件缺失时需新建 session
默认：断连 grace 30s · idle TTL 300s · replay 60s / 8 MiB。
客户端需另行停止已缓存的播放音频；session resume 依赖同一个仍存活的 API 进程。
Notes: Disconnect, response.cancel and close are different actions. A resumable session may continue generating during the disconnect grace; PersonaPlex closes. Cancel invalidates server-side in-flight/unsent output, while the client separately stops and clears audio already delivered to its playback buffer. Cancel leaves the session open; PersonaPlex resets model context. Resume credentials are session ID plus the latest token; lease-generation checks are internal engine synchronization, not an additional WebSocket client credential. Successful resumes rotate tokens. A journal gap produces session.resync_required. The session must remain on the same live API owner. Defaults are disconnect grace 30s, idle TTL 300s, replay TTL 60s and replay cap 8 MiB. A session whose session.created could not be delivered is closed immediately rather than held for an impossible resume.
Sources:
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/entrypoints/duplex/session_attachment.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/config/stage_config.py
https://github.com/vllm-project/vllm-omni/blob/4c5541cfc17143f80bdb89bbb7a5840b08bb52c6/vllm_omni/engine/duplex/session/lease.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/config/stage_config.py
https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/examples/online_serving/personaplex/README.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/docs/design/fullduplex-personaplex.md
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/deploy/personaplex.yaml
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/vllm_omni/entrypoints/duplex/serving.py
https://github.com/vllm-project/vllm-omni/blob/ee81f33001922f8d91dd09da0a57ee1531a8df82/tests/engine/duplex/test_session_runner_personaplex.py

## Slide 19
全双工
附录 · 部署
跨机 Stage 共用入口侧的 Orchestrator
单个 API worker 持有 duplex session；Head 连接本机及已注册的 headless Stage 进程。
vLLM-Omni / 实时音视频会话
2026 年 10 月
A5
Head 节点
API / EngineClient / Duplex Orchestrator
本机 Stage 0 · EngineCore / Worker
节点 B · headless
Stage 1 · EngineCore / Worker
节点 C · headless
Stage 2 · EngineCore / Worker
请求 / 输出
1 统一部署配置
统一模型拓扑；session_mode: duplex
配置设备与网络 connector
2 启动 Head
stage-id 0 启动单个 API worker 与本机 Stage
提供可访问的 master 地址与端口
3 部署侧启动 headless
指定 stage-id 与同一 master
向 OmniMaster 注册，启动本机 Stage
Headless Stage 共用 Head Orchestrator；duplex 不支持多 API worker，跨机传输需配置网络 connector。
Notes: 跨节点部署时，入口 Head 持有 API、EngineClient 和 Duplex Orchestrator，本机或远端 headless Stage 向 OmniMaster 注册，由同一入口侧 Orchestrator 调度。部署侧使用同一拓扑配置，指定 session_mode: duplex、设备与网络 connector；先启动 Head，再启动指定 stage-id 的 headless 进程。当前 duplex 不支持多个 API worker；多个 Stage 或 Replica 不意味着每个 Stage 各自持有一个 Duplex Orchestrator。
补充技术说明与参考（英文原文）
The Head process owns the API/EngineClient and its Duplex Orchestrator. It starts the selected local stage and discovers other stage/replica processes through OmniMaster registration. Each headless process starts its assigned Stage engines/workers; it does not create a separate Duplex Orchestrator for that stage.
Use a consistent deploy topology, reachable master address/port and network-capable connectors for cross-node Stage data. SharedMemory connectors are local-host transports. The Head Orchestrator dispatches to StagePool clients and preserves request affinity.
Current duplex endpoints reject configurations with multiple API workers, since attachment credentials and replay state are owner-local. Scaling stage replicas is different from scaling API workers, and a distributed Stage layout does not supply transparent frontend failover. The diagram illustrates deployment ownership; model/device/connector support must match the chosen configuration.
Sources:
- api_server.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/api_server.py
- stage_runtime.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/stage_runtime.py
- stage_init_utils.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/stage_init_utils.py

## Slide 20
全双工
附录 · 参考代码
参考代码
vLLM-Omni / 实时音视频会话
2026 年 10 月
A6
层次
实现入口
阅读重点
API 通信适配
OmniDuplexSessionHandler
协议 event、连接绑定与 replay
EngineClient
DuplexOmni / DuplexSessionHandle
handle、共享 output buffer 与 event
通信与传输
DuplexOmniEngine / DuplexOutputBuffer
控制队列与有界 session 输出
会话运行时
DuplexSessionManager / DuplexSessionRunner
lease、状态、mailbox 与模型策略
Stage 编排
DuplexOrchestrator / StagePool
初始请求、后续更新与副本绑定
模型执行
Scheduler / Model Worker
batching、计算与模型缓存
Notes: 参考代码按职责列出阅读入口：API 通信适配、EngineClient、通信与传输、会话运行时、Stage 编排和模型执行。先区分 command、控制操作结果与普通 session 输出，再对应到 Manager / Runner、StagePool、Scheduler 和 Model Worker。图中的类名与方法名保留英文，便于对应源码。
补充技术说明与参考（英文原文）
The references link to one source snapshot. The engine queue carries commands and lifecycle control messages. Ordinary output uses the handle's shared DuplexOutputBuffer; the global output queue remains for control results and exceptional session notifications. Follow Manager/Runner for session ownership, StagePool for replica selection, and Scheduler/Worker for model compute and retained caches.
Sources:
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- duplex_omni.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
- duplex_omni_engine.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex_omni_engine.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py