## Slide 1
FULL DUPLEX
The Next Inflection Point
in AI Interaction
How vLLM-Omni Enables Models to
Listen and Speak Simultaneously
vLLM-Omni / Real-time conversations
OCTOBER 2026
Notes: The Next Inflection Point in AI Interaction
How vLLM-Omni Enables Models to Listen and Speak Simultaneously
Full duplex lets models keep listening while speaking. This talk introduces the interaction modes, unified runtime architecture and measured performance of vLLM-Omni. Capabilities vary by model and execution mode.

## Slide 2
FULL DUPLEX
COMMUNITY
Full duplex, built with the community
Thanks to 60+ contributors · 160+ related PRs merged
vLLM-Omni / Real-time conversations
OCTOBER 2026
01 / 12
SELECTED MERGED PRs
AS OF 07 OCT 2026
Native duplex runtime · #3907
Unified duplex framework · #7413
OpenAI Realtime API · #7285
Qwen3-Omni integration · #7585
PersonaPlex unified duplex · #7695
Nemotron VoiceChat · #6089
AURA integration · #7633
Bounded output delivery · #7644
0xtoward
0z5a
AbelSara
akshatvishu
amy-why-3459
andyluo7
anurag12-webster
BeatSeat
BruceLoveDecimal
CarrotSwordsman
chickeyton
congw729
dshah1333
eval-dev
FayeSpica
frank-2077
Fyrgo8
Gaohan123
GKangaroo
guanzheh
herotai214
Hiro208
hsliuustc0106
HyperbolicCr
IneshReddy249
LHXuuu
linyueqian
LinzeShi
lishunyang12
LOGO127
m0g3r
MrDongsls
natureofnature
NickCao
NolenLiang
NumberWan
psv666
pujitha24
R2-Y
RyanYun09
sphinxkkkbc
StormMelody
stringl1l1l1l
Sy0307
tc-mb
TheCodeWrangler
THUqliu
Tiagosf00
tlysanhuo
twu3202
vraiti
vuuihc
wuli666
xsmccc
xuhuan51
y-null
yenuo26
yuekaizhang
ZacheryAU
ZhengWG
Zhou248
zyforsure
Notes: Full duplex is built with the vLLM-Omni community. This edition recognizes 62 GitHub-linked human contributors across 166 related pull requests merged to main through 7 October 2026. The slide uses rounded lower bounds of 60+ contributors and 160+ PRs.
The portraits credit PR authors and GitHub-linked coauthors on merged commits, in alphabetical order with equal visual weight. Scope includes duplex runtimes, associated model integration and execution, Realtime control, and direct benchmark / validation tooling. Review-only contributions are not included in this count; unlinked signatures are recorded separately without assigning an identity or portrait. Original public GitHub profile avatars link to their respective profiles.
Selected milestones connect native duplex, the unified framework, Realtime interoperability, model integrations and bounded output delivery. The complete attribution is in the companion Community Credits document.
Sources:
- https://github.com/vllm-project/vllm-omni/pull/3907
- https://github.com/vllm-project/vllm-omni/pull/7413
- https://github.com/vllm-project/vllm-omni/pull/7285
- https://github.com/vllm-project/vllm-omni/pull/7585
- https://github.com/vllm-project/vllm-omni/pull/7695
- https://github.com/vllm-project/vllm-omni/pull/6089
- https://github.com/vllm-project/vllm-omni/pull/7633
- https://github.com/vllm-project/vllm-omni/pull/7644

## Slide 3
FULL DUPLEX
EXPERIENCE & INTERACTION
vLLM-Omni / Real-time conversations
OCTOBER 2026
02 / 12
Keep the
conversation flowing.
One live conversation
Camera
User speech
Assistant speech
barge-in
01
Concurrent input & output
Keep receiving speech and video
while the assistant responds.
02
Streamed responses
Deliver text and audio incrementally,
without waiting for a complete reply.
03
Adaptive interaction
Use new input to continue, adapt what comes next, or yield the floor.
Hard interruption: forced stop
Client / server control
Explicit cancel or configured VAD policy
Soft interruption: model-driven yielding*
The model uses ongoing input + context to decide when to stop.
*Depends on model capability.
Notes: Full duplex keeps input and output active within the same session. Responses stream incrementally, while new input can affect what happens next. How that input affects generation depends on the model. MiniCPM's native policy can choose LISTEN or SPEAK; a turn-based model instead starts a new model request from committed input. The timeline is illustrative, not a latency benchmark.
Hard interruption is explicit application/server control, including configured VAD policy. Soft interruption here means model-driven yielding; semantic endpointing alone does not create native LISTEN/SPEAK capability. The client must stop and clear local playback when the protocol signals an interruption.
Sources:
- capabilities.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/capabilities.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py

## Slide 4
FULL DUPLEX
EXPERIENCE & INTERACTION
How models handle live interaction
Web demo examples: model decisions, Server VAD and client controls shape the interaction.
vLLM-Omni / Real-time conversations
OCTOBER 2026
03 / 12
MODEL
INTERACTION
WHAT HAPPENS
MiniCPM-o 4.5
Continuous speech and video input
Model decides LISTEN / SPEAK
Listen or respond within the live session
No Server VAD required by default
Qwen3-Omni
Server VAD detects user speech
Microphone input stays active
Stop queued playback
Interrupt the current response*
AURA
Hold to talk; release to submit
new audio / video input
Holding stops local playback
Server generation can continue
Applications can add explicit response.cancel for server-side cancellation.
MODEL YIELDING
The model switches to listening
LISTEN is not response.cancel
LOCAL PLAYBACK STOP
Stop what the user hears
Generation may continue
SERVER CANCELLATION
Cancel the current response
Client clears queued audio
* Server VAD interruption requires interrupt_response. Behavior depends on the model and selected demo profile.
Notes: The examples describe the MiniCPM, Qwen3-Omni and AURA Web demo profiles. Model-controlled yielding, local playback stop and server cancellation have different effects.
MiniCPM accepts continuous audio/video input and uses model-native LISTEN / SPEAK without requiring Server VAD by default. LISTEN is separate from explicit cancellation.
Qwen3-Omni's Server VAD profile keeps microphone input active, stops queued playback on speech_started and enables server interruption through interrupt_response. The separate manual Realtime profile uses duplex=0, pauses upload while answering and submits input_audio_buffer.commit followed by response.create; it is not the VAD profile illustrated in the table.
AURA's hold-to-talk action stops local playback while server generation may continue. Releasing the button commits new input. The named demo profiles do not send response.cancel; applications can integrate that command through the shared protocol. Cancellation of generation and cleanup of audio already delivered to the client are separate responsibilities.
Sources:
- qwen3_turn.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
- aura_ptt.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py

## Slide 5
FULL DUPLEX
EXPERIENCE & INTERACTION
Interfaces, interaction modes and model execution
vLLM-Omni / Real-time conversations
OCTOBER 2026
04 / 12
The interface carries the conversation; the execution mode determines how the model processes input.
Interface
Interaction
Execution
Models
Chat Completions
/v1/chat/completions
Realtime Duplex
/v1/duplex or /v1/realtime?duplex=1
Request–response
Duplex session
A request returns a response;
streaming is optional.
Native duplex execution
Continuous input and output
within ongoing inference
Turn-based execution
A new generation request
for each committed turn
Qwen3-Omni
MiniCPM-o 4.5 (turn mode)
MiniCPM-o 4.5
PersonaPlex
Nemotron VoiceChat
Qwen3-Omni + Server VAD
AURA
Realtime also supports a separate turn-based path: /v1/realtime?duplex=0.
OpenAI Realtime–based message protocol with vLLM-Omni extensions
Video input · Playback feedback · Session resume
Notes: The duplex message protocol builds on the OpenAI Realtime event vocabulary and payload structure, with vLLM-Omni extensions for video input, playback feedback and session resume. /v1/duplex is an alias of /v1/realtime?duplex=1; both use the same handler and wire protocol. This describes protocol lineage and extensions, not universal feature support or complete semantic equivalence across all models.
Reference: https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/docs/serving/realtime_duplex_api.md#compatibility-with-the-openai-realtime-protocol
Distinguish three layers: the interface, the conversation interaction, and the model execution inside a session. Chat Completions carries request–response interactions, optionally streamed. Qwen3-Omni and MiniCPM-o 4.5 in turn mode are representative examples; the list is not exhaustive.
Realtime Duplex opens an engine-owned Duplex session. Use /v1/duplex, or select the Duplex backend explicitly with /v1/realtime?duplex=1. Native duplex execution consumes ongoing input while producing output: MiniCPM-o 4.5, PersonaPlex and Nemotron VoiceChat follow this model-specific path. Turn-based execution buffers a turn and submits a new generation request when it is committed: Qwen3-Omni with Server VAD and AURA are examples. Qwen also supports explicit commit. AURA controls its turns through its model/session policy. The interface remains a streaming session for both execution modes.
Execution mode does not imply identical capabilities. Video input, cancellation, yielding, resume and concurrency vary by model. In particular, MiniCPM LISTEN/SPEAK decisions must not be generalized to every native duplex model. The same model can appear on multiple serving paths when configured accordingly.
/v1/realtime?duplex=0 uses a separate generic turn-based Realtime connection with connection-owned history and a new generation request per committed turn. It does not allocate a Unified Duplex engine session. The unqualified /v1/realtime route selects the backend according to server configuration. The explicit interface labels on this slide avoid equating every WebSocket Realtime connection with Unified Duplex.
Sources:
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/api_server.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/openai.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/realtime/connection.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/capabilities.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/personaplex/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js

## Slide 6
FULL DUPLEX
ARCHITECTURE & EXECUTION
Duplex WebSocket and Python sessions share engine-side control, model plugins and bounded output delivery.
vLLM-Omni / Real-time conversations
OCTOBER 2026
05 / 12
Unified duplex architecture, with clear roles at each layer
APPLICATION / API PROCESS
API / Python event loop
API Server
Wire I/O · attach
event replay
Python
EngineClient
handle · session API
event stream
Duplex Orchestrator
Session
Manager
1. Create / close / resume; manage leases
2. Check capacity / backlog; route commands
3. Bound session output; reap expired sessions
Session
Runner
1. One runner per session; ordered mailbox
2. Handle input, commit, cancel, Stage output
3. Advance response, history and playback
Model
Plugin
1. Capabilities; runtime / sampling settings
2. Session buffers; chunk / turn input
3. Interpret output; set downstream Stage policy
command
operation result
session buffer
same process · separate loops
API Server: protocol, attachment and event replay
EngineClient: handles, event streams and control results
Duplex Orchestrator: session execution and Stage dispatch
Stage requests
Stage output
Stage execution processes
Scheduler + workers · compute, KV and stream caches
open / close / resume
success or error
Notes: This diagram covers the engine-owned Unified Duplex path. API and Orchestrator run in the same process, on separate event loops/threads; Stage engines and workers run in separate processes. The generic turn-based Realtime handler has a different connection-owned control path.
API Server handles wire events, attachments, replay and event acknowledgements. EngineClient owns typed session handles and event iteration, passes each handle's bounded output buffer to the engine, and routes lifecycle results and exceptional notifications. Manager admits sessions, owns runner/request mappings, checks input and output limits, routes commands and reaps expired sessions. Each Runner consumes its ordered mailbox and coordinates input, response, playback and model work. Plugin supplies capabilities, model state, input construction, output interpretation and stage policies.
Open/close/resume/touch controls and ordinary commands share request_queue, but controls wait for a correlated result while commands return after enqueue. Ordinary text/audio events go directly to the registered per-session DuplexOutputBuffer shared with handle._outbox. Lifecycle results, close notifications and errors without a live output buffer use the global output queue. GPU KV and streaming compute caches belong to Stage workers.
Sources:
- duplex_omni.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
- duplex_omni_engine.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex_omni_engine.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py

## Slide 7
FULL DUPLEX
ARCHITECTURE & EXECUTION
Full-duplex workflow
API Server handles the wire protocol; EngineClient exposes session handles; Runner / Plugin drives execution.
vLLM-Omni / Real-time conversations
OCTOBER 2026
06 / 12
API / Python event loop
Dedicated orchestrator thread
Worker processes
User Client
Capture · playback
API Server
WebSocket ↔ command / event
EngineClient
session handle · output buffer
Duplex Orchestrator
Session Manager · Runner · Plugin
Stage workers
Compute · KV / cache
Session setup: EngineClient creates handle + buffer → Manager admits the session and shares that buffer → result returns
audio / video
command
Enqueue to Runner mailbox
Plugin plan → Stage request
Next input chunk arrives while Stage computation / output continues
Stage output
Per-session output buffer
handle.events() → API pump
text / audio
playback
playback ACK
command
ACK → update playback progress
Continuous input · Bounded output per session · Playback progress reported separately
Session event ACKs stay at the API. Playback ACKs reach the Runner; history updates depend on model support.
Notes: At open, EngineClient creates a handle and its output buffer; Manager admits the session and registers the same buffer object. API input is translated into commands, enqueued through DuplexOmniEngine and dispatched to the Runner mailbox. The Runner and Plugin prepare Stage requests while new input can continue to arrive.
Normal output follows Stage result → Runner/Plugin → Manager.emit → per-session buffer → handle.events() → API event pump → WebSocket. It does not pass through the global output queue first. Buffer limits are 2 MiB and 512 pending ordinary events per session by default. Output overflow fails and closes the affected session; it does not merely pause generation.
Session event ACKs update API-side replay state without entering the Runner. Playback ACKs are commands and update engine playback state according to model rules. Enqueue success is not execution completion: an engine-dead or queue-full error can be returned immediately by the API, while later command rejection is a session event.
Sources:
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- duplex_omni.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- stage_config.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/config/stage_config.py
Interaction control in the workflow: engine cancellation advances the response epoch, invalidates queued and held audio, and aborts the affected Stage requests. The API rechecks audio validity when committing delivery. Audio already delivered to the client still requires local playback cleanup. A model LISTEN transition is separate from this forced-cancellation path.
- qwen3_turn.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
- aura_ptt.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py

## Slide 8
FULL DUPLEX
ARCHITECTURE & EXECUTION
State handling: live computation and conversation history
MiniCPM updates a live request; AURA and Qwen3-Omni submit a new request for each committed turn.
vLLM-Omni / Real-time conversations
OCTOBER 2026
07 / 12
MODEL
INPUT HANDLING
STATE RETAINED ACROSS INPUTS
MiniCPM-o 4.5
Chunk → continue live request
LLM KV / audio state; configurable sliding window
AURA
Commit turn → new request
ASR text, video clips and assistant text; rebuild prompt each turn
Qwen3-Omni
Commit turn → new request
User audio, image frames and text; rebuild prompt each turn
MiniCPM-o 4.5
native duplex
Continuous audio + video
Multimodal LLM
LLM KV + streaming audio state
Talker
Per-request TTS state
Code2Wav
Decoder cache
SPEAK
LISTEN keeps the live request; later input reuses its bound Replica and retained KV.
AURA
Turn-based · audio/video commit
ASR
Audio → text
Thinker
Text + video + history
Talker
Sentence speech tokens
Code2Wav
Audio chunks
Qwen3-Omni is also turn-based: Thinker → Talker → Code2Wav, with no separate ASR Stage.
Stage = one model-compute step; Replica = an execution instance of that Stage.
MiniCPM state reuse requires a live request; AURA can continue sentence TTS within the same turn.
Notes: MiniCPM appends input to a live resumable Stage-0 request on its bound replica. It retains model KV and streaming audio state. With basic sliding-window mode enabled, its block-aligned path bounds retained context and adjusts positions using in-place Re-RoPE, rather than copying the retained KV window. The retained window is not an unlimited memory of the whole conversation. Talker/Code2Wav state follows the speech request and decoder execution.
AURA commits each turn and rebuilds its Thinker prompt from retained ASR text, video clips and assistant text. Its ASR → Thinker → Talker → Code2Wav path can continue sentence TTS within a turn; a next Thinker turn can overlap draining speech from the prior turn. Qwen similarly submits a new request for committed input, using retained audio, images and text. It has no separate ASR Stage. A commit and cancelling the current response are distinct operations.
A Stage is a compute step. A replica is an execution instance of that Stage, not a duplicate conversation history. The Session Manager and StagePool preserve request affinity needed by resident model state.
Sources:
- stage0.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/stage0.py
- window_kv.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/window_kv.py
- window_plan.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/minicpmo_4_5/duplex/window_plan.py
- plugin.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/aura_omni/duplex/plugin.py
- plugin.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py
Playback and history boundaries: playback ACKs update MiniCPM playback records without rolling back model KV. For Qwen3-Omni, complete audio and full playback ACK are required to confirm unaligned output text was fully played. AURA commits text history on Thinker completion; playback ACK does not truncate that history.
- qwen3_turn.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/qwen3_turn.js
- aura_ptt.js: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/examples/online_serving/realtime_web/app/static/profiles/aura_ptt.js
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py

## Slide 9
FULL DUPLEX
ARCHITECTURE & EXECUTION
Reconnect and continue the same session
vLLM-Omni / Real-time conversations
OCTOBER 2026
08 / 12
Reattach to a live engine session with its credentials and replay retained events from the last received position.
User Client
Present session credentials
Resume from the last received event position
API Server
Validate credentials; bind the new connection
Replay retained events
Engine session
Continue with existing session state
Reattach input and output to the same session
Requires the same live owner, a valid lease and retained events. Session resume does not provide process failover.
RESUME STEP
FRAMEWORK ACTION
USER CLIENT INTEGRATION
Session identity
Keep the same session
Python SDK retains credentials automatically;
custom clients store session ID / resume token
Connection binding
Rebind the existing session
Reconnect the WebSocket and send session.resume
Event replay
Replay retained events
Provide the last received event position
Receive retained events from the replay window
Live-session resume: MiniCPM · AURA · Qwen3-Omni · Nemotron. PersonaPlex requires a new session after disconnect.
Notes: Live-session resume is available for MiniCPM-o 4.5, AURA, Qwen3-Omni and Nemotron in their Unified Duplex paths. The client reconnects to the same live owner, sends session.resume as its first message, and supplies session ID, resume token and last received server event sequence. The server validates the lease and replay window, binds the new attachment, rotates credentials and replays retained events.
PersonaPlex currently advertises supports_session_resume=false; disconnect closes that session. Reconnect therefore opens a new one. Generic turn-based Realtime connection history is also a different path and does not use the engine-owned resume protocol.
Resume depends on the API and engine remaining alive, a valid lease and retained replay events. It is not cross-process failover. A slow or absent consumer can exhaust bounded output/replay capacity, so reconnect does not guarantee that a session will remain available indefinitely. The Python duplex client retains credentials and tracks event position for its reconnect policy.
Sources:
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py
- capabilities.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/personaplex/duplex/capabilities.py
- capabilities.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/model_executor/models/nemotron_voicechat/duplex/capabilities.py
- duplex.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/clients/duplex.py

## Slide 10
FULL DUPLEX
ARCHITECTURE & EXECUTION
Performance optimizations and steady progress
Four methods reduce repeated work and make better use of the GPU.
vLLM-Omni / Real-time conversations
OCTOBER 2026
09 / 12
CUDA Graphs: reuse prepared execution
Replay GPU work with less CPU launch overhead.
MiniCPM-o 4.5 · Qwen3-Omni (images) · PersonaPlex
Kernel fusion: combine small operations
Reduce GPU launches and intermediate data movement.
MiniCPM-o 4.5
Session batching: process streams together
Run new frames from several sessions in one batch.
PersonaPlex
Incremental decoding: handle new audio only
Skip audio that was decoded in previous chunks.
PersonaPlex
H100 · 8 concurrent requests · Seed-TTS
Chart: MiniCPM-o 4.5
| Oct 5 | Oct 6 | Oct 7 | Oct 8
Mean Audio RTF | 0.98445 | 0.743 | 0.55971 | 0.49029
Lower Audio RTF is better
Seed-TTS speech generation via Chat Completions · Daily runs, October 5–8, 2026.
Audio RTF = audio generation time / output audio duration; averaged per request.
Notes: These examples summarize representative optimizations in current mainline in terms of reduced setup, fewer small operations, and processing several live sessions together. They are model-specific capabilities, not a claim that every model enables every path.
1. MiniCPM-o 4.5 captures eligible streaming audio encoder units and vision encoder work for CUDA graph replay. Qwen3-Omni's graph path here is image-only; its video and audio paths retain their existing embedding execution. Captures depend on the supported shapes, attention configuration and deployment profile, with eager fallbacks. CUDA graphs primarily reduce repeated host scheduling and launch overhead; they do not eliminate the model's arithmetic.
2. MiniCPM-o 4.5's shared Code2Wav backend defaults to its fused CFM/DiT body on supported CUDA execution when TF32 is enabled. Smaller operations are fused to reduce launch and intermediate-memory overhead. Unsupported layouts and attention-cache types fall back, and TF32 opt-out changes the default choice. Resident slot pooling remains opt-in. Fusion may change floating-point rounding and does not guarantee identical waveforms. The recent shared output path also moves eligible GPU-to-CPU waits to output consumption, but that separate implementation detail is omitted from the visible slide.
3. PersonaPlex groups eligible live one-frame appends across sessions into a batched preparation path. Initial/persona-prefill appends and ineligible inputs use their existing path. Its asynchronous Code2Wav input contains only new codec frames; the synchronous full-payload path consumes each request once. This avoids repeatedly decoding an old prefix and should not be read as a measured throughput gain for all session mixes.
Benchmark trend: the four latest consecutive H100 daily runs in the supplied performance dataset, October 5–8, 2026, use MiniCPM-o 4.5, Seed-TTS, openai-chat-omni, configured max_concurrency=8, num_prompts=128, and the same exported config_key. Their mean_audio_rtf values are 0.9844461966498954, 0.7430039011861929, 0.559707561533549, and 0.4902875810555307. All 128 requests completed in each run. The table rounds these to two decimals. The displayed improvement is an aggregate daily trend, not an isolated A/B attribution to any optimization above. The export does not establish identical deployment flags or exact runtime commits across runs, and only labels the hardware as H100; no GPU count is inferred.
This is Chat Completions speech generation, not eight simultaneous native-duplex audio/video conversations. For the chat benchmark, audio generation time is elapsed time from request start to the final audio response chunk, and audio duration is decoded from the returned audio. Audio RTF is the per-request ratio, averaged across requests. The values do not establish first-play latency, interruption quality or uninterrupted playback under every load. No new GPU benchmark was run for this revision. Source URLs are intentionally kept in notes.
Sources:
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/streaming_audio_encoder_graph.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/encoder_cuda_graph.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/minicpmo_4_5_code2wav.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/minicpmo_4_5/dit_fused.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/qwen3_omni/vision_encoder_cudagraph.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/personaplex/duplex/stage0.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/model_executor/models/personaplex/personaplex_code2wav.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/worker/gpu_generation_model_runner.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/vllm_omni/benchmarks/patch/patch.py
- https://github.com/vllm-project/vllm-omni/blob/06afa310c942c0506f0ed9bdd189fa331c46bb97/docs/design/minicpm_o45_mrv2_performance.md
- https://github.com/vllm-project/vllm-omni/pull/8430
- https://github.com/vllm-project/vllm-omni/pull/8215
- https://github.com/vllm-project/vllm-omni/pull/8557
- https://github.com/vllm-project/vllm-omni/pull/8356
- https://github.com/vllm-project/vllm-omni/pull/7480
- https://github.com/vllm-project/vllm-omni/pull/8540
- https://hsliuustc0106.github.io/vllm-omni-kanban/pages/assets/charts/minicpmo_4_5_history.json
The four visible categories are optimization methods, with model examples listed beneath each method. CUDA Graphs reduce host launch overhead, kernel fusion reduces launches and intermediate traffic, session batching processes eligible live frames together, and incremental decoding skips already decoded audio. These categories apply to distinct paths and should not be read as four universally enabled features for every model.
PersonaPlex also has optional Mimi encode/decode CUDA graph capture: see duplex/stage0.py and personaplex_code2wav.py in the pinned mainline above. Supported capture shapes and codec graph configuration apply. Its batching example refers to eligible live frame encoding/embedding, rather than arbitrary complete conversations. Its incremental decoding example refers to async new-frame Code2Wav input.
The MiniCPM-o chart is the same four measured daily records as v57, now shown as an editable line chart with the original unrounded values embedded. It illustrates a benchmark trend; it does not attribute the observed decrease to these four methods collectively or to any single PR. PersonaPlex-only changes are not an explanation of MiniCPM-o benchmark improvements.

## Slide 11
FULL DUPLEX
EVALUATION & PERFORMANCE
From first audio to sustained conversation quality
OmniInteract and Omni-DuplexEval connect live session execution with timing and quality evaluation.
vLLM-Omni / Real-time conversations
OCTOBER 2026
10 / 12
Timing schematic
Timing origin
First audio packet received
TTFP
Request / output
Queue
Stage compute
Transfer
Incremental audio generation and delivery
Client playback
Playback starts
Playback overlaps subsequent generation
Response speed
TTFP · p50 / p95
Queue, compute and transfer
Output cadence
RTF · chunk intervals
Pauses and playback buffers
Duration and concurrency
Duration · session count
Peak memory · reclamation
Speech quality
Valid, complete audio
WER / CER · listening quality
Fix model, hardware, concurrency and timing origin. Benchmark support and evaluation tasks are model-specific.
Notes: TTFP measures the first received audio packet from a declared timing origin. It differs from audible playback, which includes client buffering and device scheduling. RTF is generation time divided by generated audio duration, so lower is better; audio duration per second is the inverse rate and should be labeled separately. Measure latency distributions, inter-chunk gaps, memory, session duration and speech quality together.
OmniInteract supplies audio/video session execution and timing/evaluation artifacts. Omni-DuplexEval supplies task-oriented native-duplex generation, timing metrics and judging, with a MiniCPM-focused runner and CI guard. Availability of benchmark code does not imply every integrated model supports every task or interaction. Keep hardware, concurrency, input timing and scoring settings fixed when comparing results.
Sources:
- omniinteract.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/omniinteract.py
- omniinteract_eval.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/omniinteract_eval.py
- omni_duplex_eval_runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/duplex/omni_duplex_eval_runner.py
- omni_duplex_eval_metrics.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/benchmarks/duplex/omni_duplex_eval_metrics.py
- README.md: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/tests/e2e/accuracy/omni_duplex_eval/README.md

## Slide 12
FULL DUPLEX
TOOL CALLING
Tool calling across duplex models
Broader model coverage and consistent behavior during tool execution.
vLLM-Omni / Real-time conversations
OCTOBER 2026
11 / 12
AVAILABLE TODAY
Qwen3-Omni Realtime
Tool parser in the turn-based Realtime path
Nemotron VoiceChat
Tool-result round trip in native duplex
UNIFIED DUPLEX ROADMAP
Model emits
Tool name + arguments
Application executes
External function
Result returns
Match the call_id
Model continues
Generate the reply
During execution | Define whether user input and speech output continue while the tool runs.
Turn safety | Handle interruption, timeouts, duplicate and late results; keep old calls from affecting a new turn.
Framework + plugins | Framework owns shared call handling; plugins adapt model formats and behavior. Extend coverage to Qwen3-Omni unified duplex, AURA and JoyAI.
Notes: Tool calling already exists in selected vLLM-Omni Realtime serving paths. This slide separates those integrations from the work to provide consistent tool behavior and broader model coverage in the unified duplex framework.
CURRENT SUPPORT
Qwen3-Omni can use the turn-based Realtime handler's tool-parser integration. The handler requires --enable-auto-tool-choice and --tool-call-parser when function tools are active, emits function-call names and argument events, includes function-call results in conversation history, and can generate a subsequent response from that history. This is a separate path from the Qwen3-Omni unified-duplex plugin, which currently raises “Qwen duplex tool calls are not implemented” when realtime_tools is configured. Do not infer that a successful Qwen Realtime tool integration demonstrates support in its unified-duplex deployment.
Nemotron VoiceChat already implements a native-duplex tool-result round trip through the unified framework. It emits function calls, accepts conversation.item.create containing function_call_output with a matching call_id, and queues the tokenized result into its function channel so that the model can continue in the live session. External tools run in the application. The current plugin accepts up to five tools and fixes tools/instructions once the system prompt is resident in model state.
UNIFIED DUPLEX ROADMAP
The common loop covers function names and arguments, application execution, correlated result return, and model continuation. Existing common function-call projection and a plugin hook provide a base. Extending this path requires complete model adapters and consistent behavior across supported models; the framework does not start from zero.
During execution: define independently whether the session continues receiving user input and whether it produces speech while an external tool runs. These are model/policy choices and must not be advertised as a universal behavior. For example, the turn-based Realtime handler suppresses further audio after it observes a tool call; this does not establish a common duplex policy for every model.
Turn safety: associate an outstanding call with its originating session/turn/response generation, define invalidation when a user interrupts or the turn is superseded, handle timeouts, suppress duplicate completion, and prevent late results from entering a newer turn. Common realtime projection already checks a matching completed call_id and rejects duplicate outputs. Those checks should be extended and applied consistently with interruption and timeout rules; this roadmap is not a claim that duplicate protection is entirely missing today. A historical matching call_id alone is not a complete specification of whether a result is still valid for the active turn.
Ownership: the framework should own shared call tracking, result validation, timeout/interruption processing, and stale-result handling. Model plugins should handle model-specific output formats, result encoding and continuation/listen/speak behavior. AURA, JoyAI and the Qwen3-Omni unified-duplex path are adaptation targets, not an assertion that their tool loops are already complete. Application code owns execution of the external function and reports its outcome.
Implementation references (snapshot d5a3380103df2fc827f095c60dbfb6e1c5655fd3):
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L386-L425
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L870-L940
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L1655-L1678
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py#L160-L169
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py#L108-L147
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py#L430-L501
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/realtime_events.py#L1080-L1126
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/realtime_events.py#L1430-L1487
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/plugin.py#L513-L523
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/session/control.py#L290-L327
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/tests/e2e/online_serving/nemotron_voicechat_realtime_duplex.py#L245-L273

## Slide 13
FULL DUPLEX
ROADMAP
Full-duplex roadmap
Near-term model integration, interaction and evaluation; longer-term session duration and serving scale.
vLLM-Omni / Real-time conversations
OCTOBER 2026
12 / 12
NEAR TERM
LONGER TERM
JoyAI integration
Bring JoyAI into the unified duplex framework
with model-specific input/output adapters
Unified tool calling
Shared call/result handling and model adapters
Interruption, timeout and stale-result handling
Semantic VAD
Turn completion based on meaning and context
Integration with commit and response policies
Broader realtime evaluation
Broader OmniInteract and Omni-DuplexEval coverage
More models, interaction tasks and regression checks
Longer sustained conversations
Bound context and history for extended audio/video
Maintain stable latency and memory as sessions grow
Scaled multi-replica serving
Higher session concurrency across Stage replicas
Session routing and ownership across API frontends
Notes: Near-term priorities center on model integration, richer interaction and broader evaluation. Longer-term priorities center on sustained conversation duration and serving scale. These priorities build on existing model integrations, evaluation runners and Stage replica infrastructure.
NEAR TERM
JoyAI integration: bring JoyAI into the unified duplex framework through model-specific input/output adapters and shared session orchestration. JoyAI already has model and pipeline code, along with an experimental full-duplex serving path; this priority is integration with the shared runtime rather than first-time model support. Integration does not imply that every model supports native LISTEN/SPEAK or every optional framework capability.
Unified tool calling: standardize function-name/argument output, application-executed functions, correlated result return and model continuation through the shared duplex runtime. Complete model adapters and consistent input/speech behavior, interruption, timeout, duplicate and stale-result handling. The framework already projects function calls and checks matching call IDs and duplicate results; Nemotron VoiceChat supplies a native-duplex function-result hook. The turn-based Realtime handler has tool-parser integration used by Qwen3-Omni, while the Qwen3-Omni unified-duplex plugin explicitly rejects realtime_tools. The priority is shared behavior and broader model coverage, including AURA and JoyAI adapters. The preceding tool-calling slide provides the detailed scope.
Semantic VAD: add meaning-aware turn-completion decisions to the session's commit and response policy. The current validator accepts server_vad only, the acoustic backend uses Silero, and a regression test explicitly rejects semantic_vad. Semantic endpointing is distinct from interruption-intent recognition and from native models' LISTEN/SPEAK decisions. Its inference should stay off the control loop and return ordered, session-scoped decisions, as described in the VAD appendix.
Broader realtime evaluation: extend model, interaction-task, duration, concurrency and regression coverage in OmniInteract and Omni-DuplexEval. Both evaluation paths are already present. Omni-DuplexEval includes generation, scoring and a MiniCPM-focused nightly CI guard. This priority expands and standardizes coverage; it does not introduce evaluation for the first time. Near-term coverage can also establish baselines for the longer-term duration and scaling work.
LONGER TERM
Longer sustained conversations: extend the duration and model coverage of real-time audio/video sessions while managing context, history, memory and latency. MiniCPM-o 4.5 already has model-specific paged-KV/sliding-window infrastructure. The roadmap concerns sustained behavior across growing conversations and more model paths, not an assertion of unlimited context or universal long-session guarantees.
Scaled multi-replica serving: raise concurrent-session capacity across Stage replicas and nodes, then extend session routing and ownership across API frontends. StagePool already chooses available replicas, binds requests and honors affinity; DuplexOrchestrator submits initial and update requests through it. Current duplex endpoints reject multiple API workers because session credentials and replay state remain local to the owning frontend. The concrete remaining direction is scalable session-aware routing, ownership and reliable cleanup while preserving model state affinity. Replica selection alone does not imply that a live model session can migrate its KV state to a different worker.
Implementation references (latest fetched mainline d5a3380103df2fc827f095c60dbfb6e1c5655fd3):
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/qwen3_omni/duplex/plugin.py#L160-L169
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/nemotron_voicechat/duplex/plugin.py#L444-L501
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/realtime/connection.py#L386-L425
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/realtime_events.py#L1430-L1487
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/turn_detection.py#L82-L99
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex/vad.py#L100-L108
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/tests/engine/duplex/test_engine_session.py#L598-L608
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/benchmarks/omniinteract.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/benchmarks/omniinteract_eval.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/benchmarks/duplex/omni_duplex_eval_runner.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/tests/e2e/accuracy/omni_duplex_eval/README.md
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/minicpmo_4_5/duplex/window_kv.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/stage_pool.py#L574-L609
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/engine/duplex_orchestrator.py#L393-L424
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/entrypoints/openai/api_server.py#L1880-L1895
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/model_executor/models/joyai_vl_interaction/pipeline.py
- https://github.com/vllm-project/vllm-omni/blob/d5a3380103df2fc827f095c60dbfb6e1c5655fd3/vllm_omni/experimental/fullduplex/joyvl/serving/server.py

## Slide 14
FULL DUPLEX
APPENDIX · ARCHITECTURE
Duplex execution: input, model computation and output
Normal output uses a bounded per-session buffer shared by the API and Orchestrator threads.
vLLM-Omni / Real-time conversations
OCTOBER 2026
A1
SAME API PROCESS
API event loop
Duplex Orchestrator thread
User Client · WebSocket
Input / requests
Output / events
API Server
↓ EngineClient · DuplexOmni
↓ DuplexOmniEngine
Protocol → handle → command / control
EngineClient → API Server
handle.events() → WebSocket
Session Manager → Runner
Ordered mailbox · session state
Model Plugin / ModelChannel
↓ StagePool → Stage client
StagePool → Runner / Plugin
Manager.emit → shared session buffer
request_queue
Janus · requests
session buffer
bounded · direct
MiniCPM-o 4.5 example
Thinker
Talker
Code2Wav
Orchestrator / llm2tts
Shared-memory connector
StagePool: select one · request affinity
One stage · replica processes
Replica 0 · EngineCore
Scheduler → GPU Worker
Replica 1 · EngineCore
Scheduler → GPU Worker
EngineCoreOutputs
Replicas can run on local or remote nodes
ZMQ
ZMQ
Notes: Read clockwise: API translates a wire event, EngineClient submits it through DuplexOmniEngine, and request_queue delivers commands or lifecycle controls to the Orchestrator. Manager selects the Runner. Plugin and ModelChannel prepare input; StagePool chooses the bound replica and submits to its EngineCore. Scheduler and workers execute the model and return Stage output.
For normal text/audio output, Manager writes directly into the registered per-session buffer. The same object is handle._outbox. handle.events() consumes it and the API pumps events to the WebSocket. The global output queue is a separate path for lifecycle results, close/expiry notifications and errors with no live registered buffer; ordinary audio does not accumulate there.
Session event ACKs are handled at the API attachment layer. Playback ACKs enter the command path. Queue-full and engine-dead errors can return immediately; later rejection arrives as an event. The MiniCPM pipeline at the bottom separates model stages from the process/replica diagram above. Network connectors are required when stages are placed on different nodes.
Session state ownership: SessionManager manages session-to-runner and request-to-session mappings, admission, leases, output bounds and cleanup. Each SessionRunner serializes operations through its mailbox and drives model submission. DuplexEngineSession holds the engine-side turn, response, epoch/fence, request-resource, history and playback state and implements the corresponding update rules. The model plugin creates model-specific session state and supplies buffering, input construction, output interpretation and downstream Stage policy. Worker processes own model KV and streaming caches.
Sources:
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- duplex_omni.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- duplex_omni_engine.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex_omni_engine.py
Session-state implementation references:
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- engine_session.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/engine_session.py
- plugin.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/plugin.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py

## Slide 15
FULL DUPLEX
APPENDIX · SESSION CONTROL
Acoustic VAD vs. Semantic VAD
Often combined: acoustic VAD finds a pause, then a turn model checks whether the user has finished.
vLLM-Omni / Real-time conversations
OCTOBER 2026
A2
COMPARISON | Acoustic VAD | Semantic VAD PROPOSED EXTENSION
Decision signal | Speech activity + a configured silence duration | Meaning and context Audio models can also use prosody
Pause handling | May commit after enough silence, even if the sentence is unfinished | Can wait longer when the utterance appears incomplete
System action | Commit after the silence threshold. Start a response if enabled. | Commit when the turn is judged complete. Start a response if enabled.
Compute & placement | Low-latency CPU inference Current: CPU thread pool | Typically more compute per decision Planned: Omni Stage for heavier models
OPEN-SOURCE EXAMPLE: SILERO VAD + PIPECAT SMART TURN v3.2
“Book me a flight for tomorrow to … [pause] … Beijing.”
1. Silero: speech / non-speech and pauses
2. Smart Turn: complete / incomplete
VAD can reduce noise-triggered events. Denoising and interruption intent detection are separate.
Session Runner owns commit and interruption. Inference is asynchronous and stale results are discarded.
Notes: Acoustic VAD classifies speech activity. A separate endpointing policy uses the detected silence duration to decide when to end a turn. The detector alone does not commit input or start model generation.
Semantic VAD is used here as an umbrella term for semantic end-of-turn detection. Such models estimate whether the user's utterance is complete, using linguistic context and, for audio-native models, cues such as intonation and rhythm. Text-based and audio-based approaches both exist.
Pipecat Smart Turn v3.2 is an open-source audio-native turn detector that predicts complete or incomplete. Its documented deployment pairs it with a lightweight VAD such as Silero. VAD identifies a pause, then Smart Turn analyzes the accumulated audio of the current turn. It does not require a separate transcript. The flight-booking sentence on the slide illustrates why an unfinished request may need more time; it is not a measured prediction from this model. This is a reference model combination, not a claim of vLLM-Omni integration.
LiveKit also documents turn detection layered on VAD. Its current audio turn detector requires VAD and adds semantic and prosodic information. These implementations support combining acoustic activity detection with a semantic completion model, rather than treating them as mutually exclusive components.
An API can nevertheless expose alternative turn-detection modes. OpenAI Realtime accepts server_vad or semantic_vad as the selected type. That configuration choice does not establish whether acoustic and semantic signals are mutually exclusive inside a provider's implementation.
Once the endpointing policy ends a turn, the session can commit input and, if configured, start a response. An incomplete prediction usually allows more listening time, subject to the system's timeout policy. Recognizing a new speech start or an intention to interrupt the assistant is a separate decision. Semantic turn completion is also distinct from a native duplex model's LISTEN / SPEAK behavior.
Semantic VAD remains a proposed extension in this vLLM-Omni deck. The inspected unified-runtime configuration accepts server_vad and rejects other turn-detection types.
References:
- https://github.com/pipecat-ai/smart-turn
- https://huggingface.co/pipecat-ai/smart-turn-v3.2
- https://docs.livekit.io/agents/logic/turns/turn-detector/
- https://developers.openai.com/api/docs/guides/realtime-vad
vLLM-Omni implementation:
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/turn_detection.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/vad.py
- https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
Compute and placement: lightweight acoustic VAD has low inference cost per audio frame. Silero's published reference reports less than 1 ms of CPU processing for a 30+ ms audio chunk. This is inference time, not end-of-turn latency: buffering, scheduling and the configured silence duration also affect when the session commits. It is not a vLLM-Omni measurement.
Semantic end-of-turn models usually analyze more context per decision, but their compute requirements depend on the model, hardware and invocation frequency. Smart Turn has a CPU implementation; its project reports inference from roughly 10 ms on some CPUs to below 100 ms on most cloud instances. Those figures use different inputs and environments from Silero's, so they do not establish a same-workload speed ratio. Gating semantic inference on detected pauses reduces invocation frequency.
For vLLM-Omni, the planned direction is to execute heavier semantic models through an Omni Stage, while retaining an offloaded CPU option for lightweight models. Stage placement is a proposed architecture, not an implemented Semantic VAD path or a guarantee of lower latency. Scheduling, transfers, queueing and batching must fit the interaction latency budget. The Session Runner still owns the decision to wait, commit or create a response.
Noise handling: VAD estimates speech activity and can suppress false speech events from non-speech noise. It does not produce a cleaned waveform, remove noise mixed with speech, or reliably exclude another person speaking in the background. Audio denoising, echo cancellation and target-speaker filtering are separate processing capabilities. The example does not imply dropping every non-speech audio chunk from a native duplex model's input.
Additional references:
- https://github.com/snakers4/silero-vad
- https://github.com/pipecat-ai/smart-turn
Runtime placement and session policy:
For the Unified Duplex path, Server VAD belongs to the Orchestrator session runtime. SessionManager supplies the process-shared Silero ONNX backend; each session keeps independent detector state. Runner offloads CPU detection to a thread pool and applies the resulting speech-onset, endpointing, commit and interruption policy on its control loop. These CPU threads remain in the API/Orchestrator process. MiniCPM native duplex does not require Server VAD by default. The generic turn-based Realtime connection is a separate control path.
Semantic VAD is a proposed extension here, not an integrated feature. A lightweight model can run in a bounded CPU pool, preferably reusing streaming ASR. A larger model can use a separate accelerator service with bounded batching latency. Decisions should carry session/input sequence/epoch so the Runner can apply them in order and discard stale work. Turn completion and model-native yielding are different decisions.
Sources:
- vad.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/vad.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py
- connection.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/realtime/connection.py
Planned semantic inference placement: keep lightweight models in an offloaded CPU pool. Audio-native models such as Smart Turn do not require ASR; text-based endpointing models may reuse a streaming transcript. Execute heavier semantic models through an Omni Stage, with bounded queues and latency-aware microbatching. This is a proposed extension. The Stage returns a completion estimate; the Session Runner owns wait/commit/response policy and validates session, input sequence and epoch before applying a result. Account for queueing and transfer overhead rather than assuming accelerator placement always lowers latency.
Additional references:
- https://github.com/snakers4/silero-vad
- https://github.com/pipecat-ai/smart-turn

## Slide 16
FULL DUPLEX
APPENDIX · SESSION CONTROL
Disconnect, cancel and close have different effects
MiniCPM, AURA, Qwen3-Omni and Nemotron support live-session resume; PersonaPlex closes on disconnect.
vLLM-Omni / Real-time conversations
OCTOBER 2026
A3
TRIGGER
IN-FLIGHT WORK
SESSION / RESUME
Disconnect · resumable model
May keep generating; journal later events
Disconnect grace; resume while the session lives
response.cancel
Cancel response; invalidate its queued audio
Session stays open; cancelled work stays cancelled
session.close / lease expiry
Terminate and clean up associated work
Session ends; create a new session
SESSION LIFETIME
Resume within the disconnect grace
Session remains on its live owner
VALID CREDENTIALS
Valid resume token
Matching lease generation
REPLAY COVERAGE
Last received event position
Required events remain available
Defaults: disconnect grace 30s · idle TTL 300s · replay 60s / 8 MiB. Resume requires the same live owner.
Notes: Disconnect, response cancellation and session termination affect different state. For a resumable model, a dropped connection can leave the engine session and in-flight generation alive during the disconnect grace. response.cancel cancels the response, invalidates old queued audio and preserves the session. session.close or lease expiry terminates the session and releases its associated work.
Resume depends on session lifetime, valid credentials and replay coverage. The same live owner must still hold the session; the disconnect grace and lease must permit reattachment. The server validates the resume token and lease generation. The client's last received event position must be covered by retained events. Resume reattaches to existing state; cancelled work remains cancelled and a closed or expired session cannot be resurrected. Main slide 08 presents the client-facing reconnection flow.
MiniCPM-o 4.5, AURA, Qwen3-Omni and Nemotron support live-session resume. PersonaPlex closes its session on disconnect. Current defaults are a 30-second disconnect grace, 300-second idle TTL, and a replay window bounded by 60 seconds and 8 MiB. These are configuration defaults, not guarantees of process failover or persistent recovery.
Sources:
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- session_attachment.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/session_attachment.py
- stage_config.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/config/stage_config.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py

## Slide 17
FULL DUPLEX
APPENDIX · DEPLOYMENT
Cross-node stages share the entrypoint Orchestrator
One API worker owns duplex sessions; the Head connects local and registered headless Stage processes.
vLLM-Omni / Real-time conversations
OCTOBER 2026
A4
HEAD NODE
API / EngineClient / Duplex Orchestrator
Local Stage 0 · EngineCore / Worker
NODE B · headless
Stage 1 · EngineCore / Worker
NODE C · headless
Stage 2 · EngineCore / Worker
Requests / outputs
1 SHARED DEPLOY CONFIG
Same topology; session_mode: duplex
Configure devices and network connectors
2 START THE HEAD
stage-id 0 starts one API worker + local stage
Publish a reachable master address / port
3 LAUNCH HEADLESS PROCESSES
Set stage-id and the same master
Register with OmniMaster; launch local stage
Headless stages share the Head Orchestrator. Duplex rejects multiple API workers; cross-node data needs a network connector.
Notes: The Head process owns the API/EngineClient and its Duplex Orchestrator. It starts the selected local stage and discovers other stage/replica processes through OmniMaster registration. Each headless process starts its assigned Stage engines/workers; it does not create a separate Duplex Orchestrator for that stage.
Use a consistent deploy topology, reachable master address/port and network-capable connectors for cross-node Stage data. SharedMemory connectors are local-host transports. The Head Orchestrator dispatches to StagePool clients and preserves request affinity.
Current duplex endpoints reject configurations with multiple API workers, since attachment credentials and replay state are owner-local. Scaling stage replicas is different from scaling API workers, and a distributed Stage layout does not supply transparent frontend failover. The diagram illustrates deployment ownership; model/device/connector support must match the chosen configuration.
Sources:
- api_server.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/openai/api_server.py
- stage_runtime.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/stage_runtime.py
- stage_init_utils.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/stage_init_utils.py

## Slide 18
FULL DUPLEX
APPENDIX · CODE REFERENCES
Code references
vLLM-Omni / Real-time conversations
OCTOBER 2026
A5
LAYER
IMPLEMENTATION ENTRY
READ FOR
API adapter
OmniDuplexSessionHandler
Wire events, attachment, replay
EngineClient
DuplexOmni / DuplexSessionHandle
Handles, shared output buffer, events
Transport
DuplexOmniEngine / DuplexOutputBuffer
Control queues; bounded session output
Session runtime
DuplexSessionManager / DuplexSessionRunner
Leases, state, mailbox, model policy
Stage orchestration
DuplexOrchestrator / StagePool
Initial / update, replica affinity
Model execution
Scheduler / Model Worker
Batching, compute, model caches
Notes: The references link to one source snapshot. The engine queue carries commands and lifecycle control messages. Ordinary output uses the handle's shared DuplexOutputBuffer; the global output queue remains for control results and exceptional session notifications. Follow Manager/Runner for session ownership, StagePool for replica selection, and Scheduler/Worker for model compute and retained caches.
Sources:
- serving.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex/serving.py
- duplex_omni.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/entrypoints/duplex_omni.py
- duplex_omni_engine.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex_omni_engine.py
- delivery.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/delivery.py
- manager.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/manager.py
- runner.py: https://github.com/vllm-project/vllm-omni/blob/712b90de9c7bc14c595b363401588a713a87c02d/vllm_omni/engine/duplex/session/runner.py